## Slide 1: EPA’s New National Ambient Air Quality Standard for Sulfur Dioxide (SO2)
Sunil Kumar
MWAQC
July 28, 2010

## Slide 2: Final Standard
New SO2 Standard (published June 22, 2010):
  1-hour SO2 standard - 75 ppb.
1971 SO2 standards:
  Annual average - 30 ppb
  24-Hour average – 140 ppb
  Both annual & 24-hour average standards above have been discontinued.

## Slide 3: Final Standard
Form of Standard –
  3-year average of the 99th percentile of the annual distribution of daily maximum 1-hour average concentrations.
Changes to SO2 monitoring network & reporting requirements.
Air Quality Index (AQI) revised based on the new 1-hour standard.

## Slide 4
Little health evidence to suggest an association between long-term exposure to SO2 and public health effects.
New 1-hour standard would better protect public by reducing people’s exposure to high short-term (5 minutes to 24 hours) SO2 concentrations.
New 1-hour standard would continue to prevent SO2 concentrations from exceeding the old 24-hour and annual standards.
Why a 1-hour standard ?

## Slide 5: Compliance with the New Standard
  Hybrid approach (monitoring/modeling) to assess compliance with the 1-hour standard
    Modeling approach - Medium to larger sources
    Monitoring approach - Smaller sources and sources not as conducive to modeling
Draft Modeling and implementation guidance expected
soon

## Slide 6: Monitoring Network
Washington region - 3 monitors needed at locations of expected maximum short-term concentrations (EPA criteria)
Existing SO2 network (of 3 monitors) - Not primarily configured for the above criteria of location.
States & EPA – Will work together on deciding monitor locations.
All new monitors operational by Jan. 1, 2013

## Slide 7: Designation Approach
Presumptive nonattainment boundary = County (unless state demonstrates otherwise)
    Different from “Nonattainment region” consisting of a group of counties approach used for ozone & PM2.5
    SO2 a local issue, not a regional issue like ozone and PM2.5
Initial designations - based on data from existing monitors and, where provided by states, appropriate modeling
Highest Design Value (2007-09 data):
  36 ppb (Alexandria, VA)

## Slide 8: Implementation Schedule
Milestone | Date
Final Rule | June 22, 2010
State Designation Recommendation | June 2011
EPA Designations | June 2012
SIP (Attainment & Unclassifiable Areas) | June 2013
SIP (Nonattainment Area) | February 2014
Attainment Date | August 2017