## Slide 1
Ozone Season Summary
2010
Joan Rohlfs
ACAC Meeting, COG
July 19, 2010

## Slide 2
Ozone Season Summary (2010)
Peak 8-Hour Ozone Concentrations (ppb)
* Analysis is based on draft data until July 19, 2010. Data is subject to change.
Data based on the 8-hour standard set at 75 ppb.
1 Code Red Day
17 Code Orange Days
22 Code Yellow Days
39 Code Green Days

## Slide 3
2010 Ozone Exceedances
Date | # of Monitors Exceeding | Highest Monitor | Highest Concentration (ppb)
5/21/2010 | 1 | Rockville | 76
5/27/2010 | 4 | HU-Beltsville | 87
6/2/2010 | 1 | HU-Beltsville | 80
6/4/2010 | 1 | HU-Beltsville | 77
6/12/2010 | 1 | Rockville | 82
6/18/2010 | 2 | Franconia | 83
6/21/2010 | 3 | Calvert Co. | 82
6/22/2010 | 5 | HU-Beltsville | 87
6/23/2010 | 1 | Calvert Co. | 76
6/25/2010 | 1 | Prince Georges Co. | 80
6/26/2010 | 1 | HU-Beltsville | 76
7/3/2010 | 3 | HU-Beltsville | 82
7/4/2010 | 5 | River Terrace | 86
7/5/2010 | 3 | Calvert Co. | 82
7/6/2010 | 10 | Prince Georges Co. | 90
7/7/2010 | 13 | McMillan Reservoir | 100
7/8/2010 | 3 | Frederick Co. | 93
7/15/2010 | 3 | Aurora Hills | 78
* Analysis is based on draft data until July 19, 2010. Data is subject to change.

## Slide 4
July 3rd to July 7th Poor Air Quality Event
High pressure & temperature.
Limited clouds allowed for intense sunlight (and record temperatures.
Usually re-circulating light winds kept bringing polluted air back into the region.
All three factors above led to conditions favorable to high ozone levels.

## Slide 5
July 7th Code Red
Chart: Temperature (DCA) & Ozone (River Terrace) (July 7th)
Temperature | 87.1 | 86 | 84 | 82.9 | 81 | 82 | 84 | 87.1 | 89.1 | 91.9 | 95 | 99 | 99 | 99 | 99 | 100.9 | 100 | 99 | 97 | 95 | 91.9 | 91 | 91 | 88
Ozone | 24 | 24 | 14 | 7 | 8 | 7 | 15 | 27 | 48 | 71 | 82 | 96 | 100 | 101 | 98 | 94 | 94 | 98 | 92 | 79 | 58 | 40 | 56
# of Monitors in Exceedance: 13
2 Monitors in Code Red (McMillan & River Terrace, DC)
Maximum 8-Hour Ozone: 100 ppb (McMillan, DC)
Wind Trajectory at 3 PM (July 7)
(500 &1000 m)

## Slide 6
24-Hour PM2.5 Concentrations (ug/m3)
* Analysis is based on draft data until July 19, 2010. Data is subject to change.
Data based on the 24-hour standard set at 35.5 ug/m3.
3 Code Orange Days
22 Code Yellow Days
54 Code Green Days
Fine Particle Summary (2010)