## Slide 1: Transportation Planning Board
AIR QUALITY CONFORMITY ANALYSIS
OF THE
2013 CONSTRAINED LONG RANGE PLAN &
FY2013-2018 TRANSPORTATION IMPROVEMENT PROGRAM
DRAFT
June 13, 2013
Technical Committee Item #3

## Slide 3: Travel model validation: background
Travel Model Adopted in 2012: Version 2.3.39
  Calibrated primarily with 2007 information:
    2007/08 Household Travel Survey
    2007 American Community Survey
    2007 traffic counts
    Transit on-board surveys
2010 model validation objectives:
  To evaluate calibrated model results against recent travel data:
    2010 traffic counts
    2010 American Community Survey
    2010 Metrorail electronic counts
    2010 Geographically Focused Household Travel Survey
  To refine the model to improve performance and forecasting ability
Validated travel model used in 2013 CLRP Analysis: Version 2.3.52

## Slide 4: Why is 2010 an Important Validation Year?
VMT and VMT per capita have not followed historic trends since 2007
Potential Reasons
  Effect of Recession
  Fuel Price Volatility
  Growing Internet-based Commerce and Communications
  Telecommuting
  Changing Travel Preferences of the “Millennials” (ages 13-30)

## Slide 5
Source: US DOT/FHWA and US Census Bureau
Chart: Year
| 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012
U.S. VMT (millions) | 1924328 | 2025586 | 2107040 | 2147501 | 2172214 | 2247152 | 2296705 | 2357587 | 2422776 | 2482201 | 2560373 | 2625363 | 2679459 | 2746926 | 2795611 | 2855509 | 2890222 | 2964789 | 2989430 | 3014371 | 3031124 | 2976528 | 2956762 | 2966963 | 2945815 | 2954394
2007 | 3500000
2010 | 3500000
U.S. VMT per capita | 7942.2865 | 8284.6398 | 8536.7741 | 8608.4469 | 8614.6633 | 8811.3346 | 8909.4645 | 9056.2516 | 9218.9718 | 9358.724 | 9561.3508 | 9714.6435 | 9825.9966 | 9691.4648 | 9770.1161 | 9887.3372 | 9919.619 | 10083.7928 | 10073.4833 | 10059.3645 | 10019.1398 | 9749.5568 | 9601.2981 | 9591.5718 | 9454.0803 | 9411.4746
Total US Vehicle-Miles and Vehicle-Miles per Capita
1987-2012
Notes: "I:\ateam\meetings_conf\techComm\2013-06-07\Copy of 12jantvt.xls"

## Slide 6
VMT for the TPB Planning Area 2005–2011
Legend:
Inner Jurisdictions:
DC, Arlington, Alexandria
Suburban Jurisdictions:
Montgomery, Prince George’s, Fairfax
Outer Jurisdictions:
Loudoun, Prince William, Frederick, Charles
Source: VDOT, MDOT, DDOT HPMS data (does not include local roads)
Chart: 
| 2005 | 2007 | 2010 | 2011
Grand Total | 108862202.5969 | 110537397.4443 | 110414456.648 | 109718194.7107
Inner Jurisdictions | 14672141.4334 | 14620969.2792 | 14597704.2002 | 14538015.2684
Suburban Jurisdictions | 69355496.522 | 70506063.1068 | 70038793.2334 | 69496852.3649
Outer Jurisdictions | 24834564.6415 | 25410365.0583 | 25777959.2144 | 25683327.0775

## Slide 7
Population for the TPB Planning Area 2005-2011
Legend:
Inner Jurisdictions:
DC, Arlington, Alexandria
Suburban Jurisdictions:
Montgomery, Prince George’s, Fairfax
Outer Jurisdictions:
Loudoun, Prince William, Frederick, Charles
Source: Round 8.2 Cooperative Forecasts-
2007 & 2011 figures are linearly interpolated
Chart: 
| 2005 | 2007 | 2010 | 2011
Grand Total | 4758429 | 4873673 | 5046509 | 5106750
Inner Jurisdictions | 917091 | 929973 | 949305 | 964499
Suburban Jurisdictions | 2831468 | 2880025 | 2952823 | 2973359
Outer Jurisdictions | 1009870 | 1063675 | 1144381 | 1168892

## Slide 8
VMT per Capita for the TPB Planning Area 2005-2011
Legend:
Inner Jurisdictions:
DC, Arlington, Alexandria
Suburban Jurisdictions:
Montgomery, Prince George’s, Fairfax
Outer Jurisdictions:
Loudoun, Prince William, Frederick, Charles
Chart: 
| 2005 | 2007 | 2010 | 2011
Grand Total | 22.8778 | 22.6805 | 21.8794 | 21.4849
Inner Jurisdictions | 15.9986 | 15.7219 | 15.3773 | 15.0731
Suburban Jurisdictions | 24.4945 | 24.4811 | 23.7193 | 23.3732
Outer Jurisdictions | 24.5918 | 23.8892 | 22.5257 | 21.9724

## Slide 9: Validation-related Changes to the Travel Demand Model
Increased non-motorized trip shares in dense-mixed use areas (Area Types 1 and 2)
  Based on comparisons with non-motorized trip shares observed in geographically focused household travel survey
  Applies to non-work purposes only (i.e. did not change work trips)
Refined highway network facility type coding
Improved estimated to observed VMT
    2012 model: 1.04
    2013 model: 1.00
Implemented several other technical adjustments to improve the performance or internal consistency of individual modeling steps

## Slide 10
Non-motorized Trip Adjustment in the Travel Demand Model
The share of non-work, non-motorized trips in dense mixed use areas has been adjusted upward
map represents the year 2010
Area Type 1
Area Type 2

## Slide 11
 | US 50 | VA 606 (Loudoun County Pkwy) |  | Northstar Blvd.
 | Northstar Blvd. To VA 606 | US 50 to 1.5 miles north of US 50 | 1.5 miles north of US 50 to Dulles Greenway | US 50 (at Northstar Blvd.) to VA 606 (at 1.5 miles north of US 50)
Current Conditions | 4/5/6 lanes, major/principal arterial | 2/4 lanes, minor arterial | 2 lanes, minor arterial | -------------
2013 CLRP (no Dulles access improvements) | 6 lanes, principal arterial | 4 lanes, minor/major arterial | 4 lanes, minor/major arterial | -------------
2013 CLRP VDOT A | 6 lanes, principal arterial | 4 lanes, minor/major arterial | 4 lanes, minor/major arterial | 4 lanes, principal arterial
2013 CLRP VDOT B | 4 lanes, limited access facility + 6 lanes, principal arterial | 4 lanes, limited access facility + 4 lanes, major arterial | 4 lanes, major arterial | -------------
2013 CLRP VDOT C (Loudoun County Comprehensive Plan) | 6 lanes, limited access facility | 8 lanes, limited access facility | 4 lanes, major arterial | -------------
VDOT Dulles Access Improvements Alternatives

## Slide 12: AIR QUALITY CONFORMITY 2013 CLRP & FY2013-2018 TIP Ozone Season VOC
Chart: Year
| 2015 | 2017 | 2020 | 2025 | 2030 | 2040
No Dulles Access Improvements | 59.2038 | 52.47 | 46.646 | 42.87 | 40.5592 | 44.0746
VDOT ALT A | 40.6 | 44.1
VDOT ALT B | 40.6 | 44.1
VDOT ALT C | 40.6 | 44.1
2009 Attainment Budget

## Slide 13: AIR QUALITY CONFORMITY 2013 CLRP & FY2013-2018 TIP Ozone Season NOx
Chart: Year
| 2015 | 2017 | 2020 | 2025 | 2030 | 2040
No Dulles Access Improvements | 133.8383 | 110.53 | 87.6708 | 72.13 | 66.9356 | 68.2164
VDOT ALT A | 67 | 68.2
VDOT ALT B | 67 | 68.2
VDOT ALT C | 66.9 | 68.2
2009 Attainment Budget
2010 Contingency Budget

## Slide 14: AIR QUALITY CONFORMITY 2013 CLRP & FY2013-2018 TIP PM2.5 Precursor NOx
Chart: Year
| 2002 | 2015 | 2017 | 2020 | 2025 | 2030 | 2040
No Dulles Access Improvements | 126953 | 46903.7612 | 38892 | 31094.687 | 25696 | 23988.9041 | 24609.4498
VDOT ALT A | 23999 | 24618
VDOT ALT B | 23997 | 24620
VDOT ALT C | 23996 | 24623
2002 N0x Level | 126953 | 126953 | 126953 | 126953 | 126953 | 126953 | 126953
Tier 1 Mobile Budgets
Tier 11 Budget
Tier 22 Budget
Tier 2 Mobile Budgets

## Slide 15: AIR QUALITY CONFORMITY 2013 CLRP & FY2013-2018 TIP Direct PM2.5
Chart: Year
| 2002 | 2015 | 2017 | 2020 | 2025 | 2030 | 2040
No Dulles Access Improvements | 3959 | 1884.9116 | 1650 | 1384.521 | 1234 | 1211.3024 | 1255.5492
VDOT ALT A | 1212 | 1256
VDOT ALT B | 1212 | 1256
VDOT ALT C | 1212 | 1256
Tier 1 Mobile Budgets
Tier 11 Mobile Budgets
Tier 2 Mobile Budgets
Tier 22 Mobile Budgets
2002 Level | 3959 | 3959 | 3959 | 3959 | 3959 | 3959 | 3959

## Slide 16
Schedule