## Slide 1: Station Pedshed and Bikeshed Atlas 2.0
TPB Bicycle and Pedestrian Subcommittee Presentation
September 17, 2024

## Slide 2: What We’ll Cover Today
Station Pedshed and Bikeshed Atlas
Introduction and Background
Methodology
Examples of Pedsheds and Bikesheds
Resources

## Slide 3: Why Atlas 2.0?
Station Pedshed and Bikeshed Atlas

## Slide 4: Your Metro, The Way Forward
Metro’s 2023 Strategic Transformation Plan prioritizes safe and accessible routes to transit for pedestrians and bicyclists.
Our goal is to increase the share of riders who access Metrorail by bicycle from 1.4% in 2024 to 3.5% by 2030.
The Station Pedshed and Bikeshed Atlas 2.0 helps Metro and our partners meet this goal.
  Understand which areas have the best existing non-auto access to stations
  Visualize barriers or gaps in the transportation network
  Identify areas with potential to unlock new ridership
Station Pedshed and Bikeshed Atlas
Four goal areas from the Strategic Transformation Plan

## Slide 5: Walking to Metro
Nearly two-thirds of Metrorail riders already reach their station by walking,1 but the share of riders accessing Metro by walking can vary drastically by station…
Station Pedshed and Bikeshed Atlas
Clarendon – 80% 🚶
1Mode of access data in this presentation are from the 2022 Metrorail Passenger Survey

## Slide 6: Walking to Metro
Nearly two-thirds of Metrorail riders already reach their station by walking,1 but the share of riders accessing Metro by walking can vary drastically by station…
Station Pedshed and Bikeshed Atlas
Clarendon – 80% 🚶
Southern Avenue – 9% 🚶
1Mode of access data in this presentation are from the 2022 Metrorail Passenger Survey

## Slide 7: Biking to Metro
Station Pedshed and Bikeshed Atlas
College Park-U of Md – 9% 🚴
Approximately 2% of Metrorail riders reach their station by bicycle or scooter (personal or shared fleet), but this also varies by station…

## Slide 8: Biking to Metro
Station Pedshed and Bikeshed Atlas
College Park-U of Md – 9% 🚴
Shady Grove – <1% 🚴
Approximately 2% of Metrorail riders reach their station by bicycle or scooter (personal or shared fleet), but this also varies by station…

## Slide 9: Why the Disparity?
Many elements influence Metro ridership and mode of access.
  Physical barriers like highways, rivers, and disjointed street and sidewalk networks
  “Traffic stress” from real or perceived safety issues on roads
Pedsheds and bikesheds allow us to visualize the areas—or actual paths—around Metrorail stations that are accessible to pedestrians, bicyclists, and micromobility users.
Station Pedshed and Bikeshed Atlas
Level of Traffic Stress (LTS) scoring (Source: Maryland Statewide Bicycle and Pedestrian Master Plan)

## Slide 10: Metrorail Walkshed Atlas 1.0
Metro debuted its Walkshed Atlas 1.0 in 2015 through the PlanItMetro blog site.
  PDF Report
  Link to GIS files provided in comments
The Atlas has not been updated since, despite the significant levels of development that have occurred over the last decade.
Station Pedshed and Bikeshed Atlas
Columbia Heights station in Walkshed Atlas 1.0

## Slide 11: What’s New in Version 2.0
For the first time at Metro, we have station bikesheds (low-stress and total networks).
New resources include…
  StoryMap
  Interactive web map with GIS data available for download
  Updated PDF report
Station Pedshed and Bikeshed Atlas
Interactive Pedshed and Bikeshed Atlas 2.0 Web Map

## Slide 12: How We Made the Atlas 2.0
Station Pedshed and Bikeshed Atlas

## Slide 13: Step 1: Gather Geospatial Data
For pedsheds, the project team used sidewalk and crosswalk data to establish a sidewalk network.
For bikesheds in DC and Maryland, the team used street-level Level of Traffic Stress (LTS) measures to develop a street network.
For bikesheds in Virginia, where LTS measures were not readily available, we used Functional Roadway Classifications and speed limits as proxies for LTS.
Station Pedshed and Bikeshed Atlas
LTS measures near College Park-UMD station from Maryland DOT

## Slide 14: Step 2: Clean and Review Network
When sidewalks or roads did not line up across jurisdictional boundaries, we manually connected these segments to reflect complete networks.
The team reviewed sidewalk and street networks by comparing it with recent satellite imagery.
Station Pedshed and Bikeshed Atlas
DDOT sidewalk data near Takoma station ends at the DC-Maryland line

## Slide 15: Step 3: Run Network Analysis
Pedsheds
We used a half-mile distance from the station as the cutoff along the sidewalk network.
Bikesheds
For low-stress networks, we included roads with LTS levels 1 through 3,2 up to three miles from a station. In Virginia, our proxy measure included roads with speed limits up to 30 MPH.
For total networks, we included all on-road facilities that could accommodate bicycle travel within three miles from a station.
The analysis generated footprints out from stations along actual paths accessible to pedestrians and bicyclists on suitable infrastructure.
Station Pedshed and Bikeshed Atlas
2LTS levels 1 through 3 include dedicated (e.g., bicycle lane) and shared (e.g., bicycle boulevard) bicycle facilities.

## Slide 16: Step 4: Describe Characteristics of Sheds
The pedshed or bikeshed size is the physical area for the polygon as measured in square miles.
Household and employment totals were obtained from demographic and business location files available from Esri.
Station ridership was obtained from Metro’s Ridership Data Portal.
Station Pedshed and Bikeshed Atlas
Example of pedshed characteristics

## Slide 17: Methodology Limitations
The LTS proxy in Virginia likely includes roads not suitable for biking (and excludes facilities that are).
This initial dataset focuses on on-road LTS, which does not include off-road bicycle facilities like multi-use trails. Future iterations of the Atlas will seek to include these facilities.
Across all 98 stations, some connections are likely missing from our data that were not identified in manual review.
Station Pedshed and Bikeshed Atlas
Off-road bicycle facilities will be included in future iterations of the Atlas

## Slide 18: Examples from the Atlas 2.0
Station Pedshed and Bikeshed Atlas

## Slide 19: PDF Maps
Station Pedshed and Bikeshed Atlas
½ Mile Radius
½ Mile Shed
Station Name and Legend
Shed Characteristics
3 Mile Radius
3 Mile “Total” Shed
Low-Stress Shed

## Slide 20: StoryMap and Web Map
Station Pedshed and Bikeshed Atlas
Pedshed and Bikeshed Atlas 2.0 StoryMap
Pedshed and Bikeshed Atlas 2.0 Web Map

## Slide 21: Initial Analysis
As a station’s pedshed size increases, we can generally expect pedestrian mode of access share to increase, as well
We find less of a relationship between bikeshed size and bicycle access
Station Pedshed and Bikeshed Atlas
Chart: Pedestrian Access and Pedshed Size
Systemwide Average

## Slide 22: Resources
wmata.com/initiatives/pedshed-and-bikeshed-atlas/
Station Pedshed and Bikeshed Atlas

## Slide 23: Thank you!
Station Pedshed and Bikeshed Atlas
Ryan Yowell
Senior Planner
ryowell@wmata.com
Seth Garland
Director of Station Planning
sgarland@wmata.com
Project Contacts