## Slide 1
Bus Priority Best Practices in the national capital region
Slide Deck This slides in this deck are intended for use by member agencies of the National Capital Region Transportation Planning Board. Open use and adaptation are permitted. Please retain all photo credits and references. Please credit the TPB as appropriate.

## Slide 2
Contents
Introduction and purpose
Results of TIGER Bus Priority in the NCR
Results of Other Bus Priority in the NCR
Bus Transformation Project (BTP) Recommendations
Key Information from Literature on Benefits and Costs of Bus Priority
Key Information from Peers on the Benefits and Costs of Bus Priority
Near Term and Future Bus Priority Projects in the NCR
TPB Bus Priority Synthesis
November 2020

## Slide 3
Introduction and purpose

## Slide 4
Nine local bus operators in the National Capital Region (NCR) provide over 164 million trips annually. Eighty-one percent of the region’s population, and 94 percent of the region’s transit dependent population live within a quarter-mile of transit. However, bus speeds and reliability have declined over the past decade, limiting residents’ access to jobs and opportunities. Metrobus speeds, for example, have decreased by 9% or 1 mph over the past 10 years.
The Bus Priority Best Practices Synthesis is a resource for the National Capital Region (NCR) highlighting local examples of bus priority and includes a comprehensive list of resources for planners and policymakers.
Photo Source: Floating Bus Stop (BeyondDC/Flickr), Data Source: National Transit Database
TPB Bus Priority Synthesis
November 2020

## Slide 5
Investing in bus priority treatments has positive impacts
Bus priority treatments can improve bus speed, reliability and efficiency
  Increasing the region’s residents’ access to jobs and opportunities
  Attracting new transit riders and improving the experience of existing riders
16th Street NW Buses (DDOT/https://www.16thstreetnwbus.com/)
TPB Bus Priority Synthesis
November 2020

## Slide 6
Results of Bus Priority Projects in the Region
TPB Bus Priority Synthesis
November 2020
Bus priority treatments lead to increased speeds and increases in ridership
Priority Bus Corridors/Services | Results | Bus priority infrastructure
Metroway | 83% ridership increase | Partial dedicated right-of-way, consolidated bus stops
H & I Streets NW Bus Lanes | 1 mph increase in bus travel speeds | Dedicated right-of-way
US 29 FLASH | 54%* ridership increase | Bus-on-shoulder lanes, TSP
16th Street NW Bus Improvements | 2-5 minutes in travel time savings* | Queue jump lanes, TSP, dedicated right-of-way
*Expected results based on ridership and/or travel time improvement forecasts
Sources: Ethan Goffman, “Northern Virginia’s Metroway Corridor Shows How Buses and Trains Can Complement Each Other,” Mobility Lab, September 30, 2019, https://mobilitylab.org/2019/09/30/northern-virginias-metroway-corridor-shows-how-buses-and-trains-can-complement-each-other/.
US29 Bus Rapid Transit Project, https://www.ridetheflash.com/wp-content/uploads/2019/09/US29FLASH-Description-March2017.pdf
DDOT, “16th Street NW Bus Lanes Project Online Open House,” https://www.16thstreetnwbus.com/wp-content/uploads/2018/07/16th-St-Online-Public-Meeting-072718.pdf
Christina Moscardi, “How well do DC’s red-painted bus lanes work?”, February 20, 2020, http://www.christianmoscardi.com/blog/2020/02/20/dc-bus-lanes.html

## Slide 7
Bus Priority Treatment Impacts Include
TPB Bus Priority Synthesis
November 2020
Reduced congestion
Improved air quality
Increased revenue from increased ridership
Reduced fuel cost from reduced delay
For more information, see: https://www.transit.dot.gov/sites/fta.dot.gov/files/CBRT_2009_Update.pdf

## Slide 8
Treatments Effectiveness Varies
Lower cost treatments can be easier to implement, but can be less impactful than higher cost treatments
  An on-road painted bus lane is less expensive to implement, but may not be as effective as a dedicated busway
Combining multiple treatments requires a larger investment, but usually results in greater improvements
Difficulty of implementation is varied and site specific, but the level of effort increases as more treatments are combined together
TPB Bus Priority Synthesis
November 2020

## Slide 9
 | Dedicated Bus Lanes/Guideways | Lanes are restricted to buses through signage or barriers Lanes could be separate from traffic, concurrent with traffic, contraflow with traffic, or shoulder lanes
 | Transit Signal Priority | Allows vehicles to communicate with traffic signals to adjust light timing Typically either extends the green light or shortens the red
 | Queue Jumps | Transit-only lanes at or before an intersection that allow buses to skip the queue of vehicles waiting a traffic light
 | Parking Limitations | Reduces the ease of parking by increasing the parking fee or reducing the number of parking spaces to encourage more people to take the bus
 | Stop Consolidation | Reduces the frequency of stops which increases the average speed of the buses
 | Off-Board Fare Payment | Allows riders to pay in advance for their ticket, which saves time in the boarding process
 | All-Door Boarding | Passengers that pay in advance can board from the rear doors, doubling the number of people that can board the bus at any given time
Bus Priority Treatments
TPB Bus Priority Synthesis
November 2020
2x
Notes: Examples of the bus priority types discussed in the syntheses. This is not a comprehensive list of all bus priority types, but provides an overview of those commonly used or discussed for potential use in the NCR.

## Slide 10
Queue jump lanes combine a short, dedicated transit facility with a leading bus interval or active signal priority
Allows buses to enter traffic in a priority position
Can reduce bus delay significantly as buses are able to the front of a queue of cars at traffic signals
  Queue Jumps become increasingly effective as road congestion increases
Queue Jumps and Bus Only Signals
TPB Bus Priority Synthesis
November 2020
Source: Queue Jump Lanes, Transit Street Design Guide (NACTO/https://nacto.org/publication/transit-street-design-guide/intersections/intersection-design/queue-jump-lanes/)
Source: Queue Jump Lanes (NACTO/https://nacto.org/publication/transit-street-design-guide/intersections/intersection-design/queue-jump-lanes/)

## Slide 11
Operates with sensors imbedded on buses and road infrastructure
Communication between buses, on-road infrastructure, and traffic management center via cellular network
Components of Transit Signal Priority
TPB Bus Priority Synthesis
November 2020
Photo Source: Components of TSP (Kittelson & Associates, Inc)

## Slide 12
Bus Priority Costs and Impacts
TPB Bus Priority Synthesis
November 2020
*TSP implementation can be costly and time consuming due to variations in technology and hardware
Source: Washington Area Bus Transformation Project, https://bustransformationproject.com/; King County Metro, Transit Speed and Reliability Guidelines and Strategies, https://kingcounty.gov/~/media/depts/transportation/metro/about/planning/speed-reliability-toolbox.pdf
Improvement | Improvement Description | Cost to Implement | Degree of Difficulty to Implement | Cost Savings/ Performance Improvements | Level of Anticipated Improvement
TSP installed at some intersections, operated conditionally | Installed at some intersections, operated on a conditional basis | $0.3M to $9.0M per mile | Low to Moderate* | 8% in travel time savings; $0.2M to $1.6M cost savings annually | Low
Dedicated lane on existing road | Dedicated lane on existing road | $0.2M to $1M per mile | Low | $0.25M in savings per year; 10-14% travel time savings; up to 27% increase in reliability | Moderate
Dense network of TSP and queue jumps at some intersections | Dense network of TSP and queue jumps at some intersections | $0.3M to $20M per mile | Low to Moderate* | 1-10% in travel time savings; $0.3M to $1.7M cost savings annually | Low
Dense network of TSP, queue jumps at all intersections, dedicated lanes on full route | Dense network of TSP, queue jumps at all intersections, dedicated lanes on the full route | $5.0M to $50M per mile | Moderate to High | 18-54% in travel time savings; $0.55M to $1.95M in cost savings annually | Moderate to High
Dense network of TSP, exclusive bus right-of-way | Dense network of TSP, exclusive bus right-of-way | $30M to $80M per mile | High | 18-66% in travel time savings; $0.55M to $1.8M cost savings annually | High

## Slide 13
Results of tiger bus priority in the ncr

## Slide 14
TIGER Bus Priority in the NCR
The US Department of Transportation (USDOT) awarded a $58.8 million TIGER grant to the National Capital Region Transportation Planning Board (TPB) for Priority Bus Transit in the National Capital Region in 2010.
Photo Source: Bus queue jump signal, 16th St DC (BeyondDC/Flickr)
TPB Bus Priority Synthesis
November 2020

## Slide 15
TIGER Bus Priority in the NCR
TPB Bus Priority Synthesis
November 2020
Five local governments or transportation agencies were responsible for carrying out the 16 individual corridor projects of the overall regional TIGER project
The improvements in technology and physical infrastructure aimed at making buses reliable and convenient in the region
TIGER-funded enhancements on eight key bus priority corridors included the following bus priority infrastructure:
  Dedicated bus lanes/guideways
  Transit Signal Priority (TSP)
  Queue Jumps

## Slide 16
TIGER Corridors with Bus Priority Infrastructure
TPB Bus Priority Synthesis
November 2020
Corridor | Dedicated bus lanes/ guideways | Transit Signal Priority (TSP) | Queue Jumps
16th Street NW, DC | - | 31 | 1
Georgia Avenue NW, DC | 0.3 mi | 57 | 3
Wisconsin Avenue, DC | - | 39 | -
US 1 Transitway, VA | 0.8 mi | - | -
VA 7 (Leesburg Pike), VA | - | 25 | -
Van Dorn – Pentagon, VA | - | 9 | 2
T. Roosevelt Bridge to K St. NW, DC* | - | 68** | -
14th Street Bridge to K St. NW, DC* |  |  | 
*TR Bridge to K St and 14th St Bridge to K St corridors are treated as two separate corridors for performance monitoring and reporting, despite sharing the same bus priority enhancements in central Washington, DC. **In addition to TSP, these corridors included signal optimization at 197 intersections and uninterruptible power supply (UPS) at 30 locations.

## Slide 17
TIGER Corridors Map
TPB Bus Priority Synthesis
November 2020

## Slide 18
On-Time Performance Results
TPB Bus Priority Synthesis
November 2020
*After measures are of two years after the enhancement implementation.
** OTP average of all WMATA routes on the corridor.
Corridor | AM Peak | Midday | PM Peak
16th Street NW | 79% | 86% | 76%
Georgia Avenue NW | 76% | 77% | 57%
Wisconsin Avenue | 73% | 65% | 57%
US 1 Transitway** | 91% | 84% | 89%
VA 7 (Leesburg Pike)** | 86% | 85% | 66%
Van Dorn – Pentagon** | 90% | 89% | 82%
WMATA priority routes on-time performance after* TIGER-funded enhancements
Arrows represent OTP increase or decrease compared to values before the enhancements

## Slide 19
TIGER Key Takeaways
TPB Bus Priority Synthesis
November 2020
On-time performance improved significantly at all time periods on the US 1 Transitway and Van Dorn – Pentagon corridors
On-time performance improvement during morning peak period was limited on Wisconsin Avenue but significant on VA 7 (Leesburg Pike)
Off-peak on-time performance improved on all corridors (where the measure was tracked)
Limited success on peak periods may be explained by heavier and more variable traffic compared to midday
Changes in passenger trips on the corridors were mostly aligned to changes in level of service and overall ridership in the region

## Slide 20
TIGER Key Takeaways
TPB Bus Priority Synthesis
November 2020
Corridor | Bus Priority Treatments | On-time Performance |  | Ridership
 |  | Peak | Off-Peak | 
16th Street NW, DC |  |  |  | 
Georgia Avenue NW, DC |  |  |  | 
Wisconsin Avenue, DC |  | - |  | 
US 1 - Transitway, VA |  |  |  | 
VA 7 (Leesburg Pike), VA |  | - | - | 
Van Dorn – Pentagon, VA |  |  |  | 
T. Roosevelt Bridge to K St. NW, DC* |  | - | - | 
14th Street Bridge to K St. NW, DC* |  |  |  | 
Notes: 16th Street NW: OTP decreased on both AM and PM Peaks; Number of trips on the corridor remained stable but ridership on the corridor decreased overall – S1 ridership increased
Georgia Ave: OTP decreased on both AM and PM Peaks; Number of trips on the corridor increased but ridership on the corridor decreased overall
Wisconsin Ave: OTP increased on the AM Peak, but not PM Peak; Number of trips and ridership increase
US 1 – Transitway: OTP and ridership increased
VA 7 Leesburg: OPT increased in the AM Peak, but decreased in the PM Peak; ridership decreased despite increase in number of trips
Van Dorn – Pentagon: OTP increased in all time periods; ridership decreased despite increase in number of trips
TR and 14th St. Bridges to K St. NW: OTP not tracked; number of trips crossing TR Bridge increased, but number of trips and overall ridership on both corridors decreased

## Slide 21
Results of other bus priority in the ncr

## Slide 22
Map of Existing Bus Priority Projects
TPB Bus Priority Synthesis
November 2020

## Slide 23
Bus Priority Planning Efforts: Washington DC
TPB Bus Priority Synthesis
November 2020
14th Street NW Bus Lane Decongestion Project
16th Street NW Bus Lane Project
K Street Transitway
Pennsylvania Avenue SE Corridor Study

## Slide 24
Bus Priority Planning Efforts: Montgomery County
TPB Bus Priority Synthesis
November 2020
US 29 BRT
MD 355 BRT
Veirs Mill BRT

## Slide 25
Bus Priority Planning Efforts: Prince George’s County
TPB Bus Priority Synthesis
November 2020

## Slide 26
Bus Priority Planning Efforts: Alexandria
TPB Bus Priority Synthesis
November 2020
Transitway Corridor B
Transitway Corridor C
Envision Route 7
Alexandria Transit Vision Plan

## Slide 27
Bus Priority Planning Efforts: Arlington County
TPB Bus Priority Synthesis
November 2020
Envision Route 7

## Slide 28
Bus Priority Planning Efforts: Fairfax County
TPB Bus Priority Synthesis
November 2020
Embark Richmond Highway Bus Rapid Transit (Route 1 BRT)
Envision Route 7

## Slide 29
Metroway, Alexandria and Arlington, VA
A continuation of TIGER funded investments in Northern Virginia
BRT Route operated by WMATA between the Pentagon City and Braddock Road Metrorail stations
Dedicated right-of-way between:
  Potomac Avenue and East Glebe Road
  South Glebe Road and Pentagon City Metrorail station
Source: Metroway, http://metrowayva.com/
TPB Bus Priority Synthesis
November 2020

## Slide 30
Between September 2014 and September 2019, monthly ridership increased from 30,000 trips to 55,000 trips
Ridership on Metroway exceeds ridership on the route it replaced
Metroway works in tandem with Metrorail service
  Metroway ridership increased 60 percent in 2019 during Metrorail station construction along Metroway’s route
Metroway
TPB Bus Priority Synthesis
November 2020
Source: Ethan Goffman, “Northern Virginia’s Metroway Corridor Shows How Buses and Trains Can Complement Each Other,” Mobility Lab, September 30, 2019, https://mobilitylab.org/2019/09/30/northern-virginias-metroway-corridor-shows-how-buses-and-trains-can-complement-each-other/.
Photo Source: Metroway Route (Metroway/http://metrowayva.com/)

## Slide 31
DDOT Bus Priority Plan and Program
Development for DDOT’s Bus Priority Plan began in 2020
The plan will include:
  Toolbox of improvements that address bus speeds and reliability
  Identify a pipeline of bus priority projects in DC
Numerous projects are underway through DDOT’s initiative:
  Three temporary Car Free Lanes or Streets
  14th Street NW Traffic Decongestion and Bus Improvements (under construction)
  16th Street NW Bus Lanes (under construction)
  K Street Transitway (future project)
  Pennsylvania Avenue SE Corridor Study (future project)
Photo Source: Bus Only Lane (BeyondDC/Flickr)
TPB Bus Priority Synthesis
November 2020

## Slide 32
H and I Streets NW see up to 70 buses per hour during peak periods and carry one-fifth of bus riders in the District
Before interventions, bus speeds were as low as 2.8 miles per hour on some segments
Bus lane pilot implemented June-September 2019, operating during peak periods; made permanent in November 2019
  Located on H Street NW between Pennsylvania Avenue NW and 14th Street NW and on I Street NW between 13th Street NW and 20th Street NW
  Operate from 7:00 a.m. and 7:00 p.m. Monday through Saturday
  Loading zones on the opposite side of the street
  Signal sequencing and operations updated to accommodate right turning vehicles
  Bus layover spaces moved outside the bus lane corridor
H and I Streets NW Bus Lanes
TPB Bus Priority Synthesis
November 2020
Source: H & I Streets NW Bus Lane (DDOT/https://ddot.dc.gov/node/1399471)

## Slide 33
Increases in bus speeds inconsistent during the pilot period
Overall average bus speeds increased by approximately one mile per hour on both corridors
Before and during the pilot period travel speeds in the AM peak were faster than the PM peak on both corridors
H and I Streets NW Bus Lanes
TPB Bus Priority Synthesis
November 2020
Source: H Street Bus Lane (BeyondDC/Flickr) (Top)
H and I Streets NW Bus Lane map ((DDOT/DDOT) (Bottom)
Christina Moscardi, “How well do DC’s red-painted bus lanes work?”, February 20, 2020, http://www.christianmoscardi.com/blog/2020/02/20/dc-bus-lanes.html

## Slide 34
DDOT 2020 Temporary Car Free Lanes or Streets
Part of the District’s COVID-19 recovery
Car free lanes support improved efficiency in bus travel and create space for cyclists
Car free lanes designated by red paint on:
  Martin Luther King, Jr. Avenue SE
  M Street SE
Car free street designated by red paint on:
  7th Street NW (bus, bike, and truck only)
  Photo Source: Bus Only Lane (BeyondDC/Flickr)
TPB Bus Priority Synthesis
November 2020

## Slide 35
DDOT 2020 Car Free Lanes
TPB Bus Priority Synthesis
November 2020
Location | Features | Travel Lane Loss | Parking Losses? | Time Enforced
7th Street NW between Massachusetts Avenue NW and Pennsylvania Ave NW | Buses, bikes, and trucks only; expanded sidewalks, loading and pick-up/drop-off zones on side streets | Yes | All metered parking is removed | 24 hours a day, seven days a week
Martin Luther King, Jr Avenue SE between W Street SE and St. Elizabeth’s East Campus | Peak hour, peak direction bus lanes; bikes allowed in bus lane | During peak hours | Minimal to no spot removal | Peak Hour
M Street SE between Half Street SE and 10th Street SE | Peak hour, peak direction bus lanes; bikes allowed | During peak Hour | Minimal to no spot removal | Peak Hour
Source: Car Free Lanes for Buses and Bikes (DDOT/https://ddot.dc.gov/node/1484591)

## Slide 36
First implemented in 2016 through TIGER grant
Operates in the District at 179 intersections and 11 Metrobus routes and in Alexandria on four corridors
Improves schedule reliability and, in non-downtown corridors, reduces schedule runtime
Less restrictive parameters to trigger extended red or green signals help increase the number of buses that can benefit from TSP
TSP has not adversely impacted performance of other modes
WMATA/DDOT TSP and Queue Jumps
TPB Bus Priority Synthesis
November 2020
Source: TSP (MDOT MTA/BaltimoreLink Transit Priority Toolkit)

## Slide 37
Bus transformation project (BTP) Recommendations

## Slide 38
Bus Transformation Project
Developed and shaped by a broad range of stakeholders and the public from across the region, the Bus Transformation Project developed a regional Strategy and Action Plan that focus on improving customer experience, connecting the region through better bus service, and fostering collaboration across transit and roadway agencies.
Photo Source: https://bustransformationproject.com/wheaton-metrorail/
TPB Bus Priority Synthesis
November 2020

## Slide 39
The BTP gathered input from people across the region which was used to recommend changes to the bus system
This feedback, complemented by extensive research and analysis, guided the development of a bold, new vision and a series of recommendations to guide the future of bus in the region
These recommendations are meant to make bus more reliable, frequent, affordable, and coordinated
The Strategy recommends concrete actions to transform existing bus services into a truly integrated, accessible regional bus network that is part of the larger regional mobility system
The Action Plan highlights the tactical activities required to achieve the changes envisioned for the region’s bus system
Bus Transformation Project
TPB Bus Priority Synthesis
November 2020

## Slide 40
Bus Transformation Project The Vision
Bus will be the mode of choice on the region’s roads by 2030, serving as the backbone of a strong and inclusive regional mobility system that will support a growing and sustainable economy.
Photo Source: Metroway (BeyondDC/Flickr)
TPB Bus Priority Synthesis
November 2020

## Slide 41
BTP – Timeline and Timeframe
SUMMER 2019
JAN 2020
SPRING 2019
SEP 2018
NOV 2018
TPB Bus Priority Synthesis
November 2020
Notes: Between 2018 and 2019, input from stakeholders, riders, and the public and extensive research and analysis formed the basis of the Bus Transformation Strategy.
The Action Plan factor in existing work of operators and jurisdiction and guide how to make the recommendations a reality over the next 10 years.

## Slide 42
BTP Recommendations
Photo Source: Bus Transformation Project Strategy Summary
TPB Bus Priority Synthesis
November 2020

## Slide 43
To give bus priority on roadways to move people quickly and reliably:
  Obtain commitments from state and local agencies (including roadway owners) to adopt consistent guidelines, bolster jurisdictional capital spending, and expedite coordinated implementation of bus priority
  Implement enforcement policies that establish bus priority and result in reliable and fast service
  Establish a capital program at WMATA that supports accelerated implementation of bus priority projects, including BRT
  Support regional congestion mitigation efforts that bolster bus priority and move more people more efficiently
Recommendation #2 Priorities
F
G
H
I
TPB Bus Priority Synthesis
November 2020

## Slide 44
How BTP Aims to Transform Bus Service
TPB Bus Priority Synthesis
November 2020

## Slide 45
Key information from literature on benefits and costs of bus priority

## Slide 46
Benefits of Bus Priority – Faster Speeds
TPB Bus Priority Synthesis
November 2020
Bus priority treatments increase the average speed of a bus by separating it from congestion and giving it an advantage at intersections
Dedicated right-of-way saves… 2 to 3 minutes per mile
Bus lanes on arterial streets save… 1 to 2 minutes
per mile
The addition of a dedicated bus lane on a congested road can double or triple the average bus speed
Photo credit: Portland dedicated busway (J.Mause/Bikeportland.org)
For more information, see https://www.vtpi.org/blw.pdf & https://nacto.org/wp-content/uploads/2015/04/tcrp118brt_practitioners_kittleson.pdf

## Slide 47
Benefits of Bus Priority – Higher Ridership
TPB Bus Priority Synthesis
November 2020
Increased speeds are associated with more efficient transit, which increases ridership
Priority Bus Corridors/Services | Approximate ridership increase | Bus priority infrastructure
Albuquerque Rapid Transit | 67% | Dedicated right-of-way, TSP
Seattle RapidRide | 87% | Dedicated right-of-way, queue jump, bus bulbs, TSP
Minneapolis METRO A and METRO C | 33% | TSP, off-board ticketing
SFMTA Muni Forward | 8% | Transit-only lanes in mixed traffic, bus-bulbs, TSP
NYC Bus Lanes | 14%* | Transit-only lanes in mixed traffic
For me information, see: https://www.transit.dot.gov/sites/fta.dot.gov/files/CBRT_2009_Update.pdf, https://kinder.rice.edu/urbanedge/2020/02/06/how-brt-service-rapidly-improved-ridership-twin-cities
https://www.masstransitmag.com/management/press-release/12383795/abq-ride-art-system-receives-rare-gold-standard-from-itdp
https://www.sfmta.com/projects/16th-street-improvement-project-phase-1-and-phase-2
https://kingcounty.gov/depts/transportation/metro/travel-options/bus/rapidride.aspx
https://wcbs880.radio.com/articles/news/nyc-adding-20-new-miles-of-busways-bus-lanes
*Example ridership increase when dedicated bus lanes were added to 14th Street

## Slide 48
TPB Bus Priority Synthesis
November 2020
Benefits of Bus Priority – Development
Bus prioritization is a catalyst for Transit Oriented Development (TOD)
Prioritization corridors are associated with an increase in property development and higher land values at the corridor level and in the area directly surrounding the corridor
Source: https://www.fdot.gov/docs/default-source/transit/documents/FDOTCO_ANationalSynthesisofTransitinCompleteStreets_FinalReport_20180508.pdf
Photo Source: Cleveland’s HealthLine (Center for Neighborhood Technology/Flickr)

## Slide 49
Costs of Bus Priority - Monetary
TPB Bus Priority Synthesis
November 2020
Mixed Traffic
Busway
Median Busways
Guided Busway
Bus Tunnel
$272 Million
$7.5 Million
$6.6 Million
$4.7 Million
$1 Million
For more information, see: https://nacto.org/docs/usdg/tcrp_rpt_90_implementation_guidelines_volume_2_levinson.pdf
Notes: Photo credits
Bus Tunnel: Photo Credit: Downtown Seattle Transit Tunnel (Heidi Groover/ Seattle Times)
Busway: Photo Credit: Ctfastrak buses (Lochner)
Median Busways: Photo Credit: Dedicated median busways (D. Hidalgo/ EMBARQ)
Guided Busway: Photo Credit: Elevated bus guideway (Urban Transport News)
Mixed Traffic: Photo Credit: Richmond Pulse Dedicated Bus Lane (Wyatt Gordon/ Greater Greater Washington)

## Slide 50
Example Bus Priority System Costs
TPB Bus Priority Synthesis
November 2020
Richmond Pulse
$8.7 million per mile
Three miles of dedicated bus lanes
7.6 miles in total
Albuquerque Rapid Transit
$15.2 million per mile
97% of the alignment is dedicated
Approximately nine miles in length
CTfastrak
$65.2 million per mile
9.4 miles of fully dedicated right-of-way
Photo Credit: Richmond Pulse corridor
(Dan Malouff/Greater Greater Washington)
Photo Credit: Albuquerque Rapid Transit bus
(HDR)
Photo Credit: CTfastrak Vehicle
(Sean Teehan/Hartford Business Journal)

## Slide 51
Costs of Bus Priority – Nonmonetary
TPB Bus Priority Synthesis
November 2020
Right-of-way space
Dedicating existing lanes to buses reduces the space available to other vehicles which can temporarily exacerbate congestion
Vehicle Crowding
Increasing the frequency and speeds of buses makes them a more attractive way to travel, which increases the ridership and can lead to bus crowding
Photo Credit: Mock-up of bus priority lanes in Nashville
(Joey Garrison/ Tennessean)
Photo Credit: Crowded BRT bus in Las Vegas
(Nick Christensen/ Oregon Metro News)
For more information, see: https://www.transit.dot.gov/sites/fta.dot.gov/files/CBRT_2009_Update.pdf

## Slide 52
Challenges of Bus Priority – Bus Lane Management
TPB Bus Priority Synthesis
November 2020
Stakeholder Coordination
Enforcement
Legislation
Education
Monitoring
One of the challenges of maintaining a bus priority system is enforcing the function of the dedicated lanes. This is particularly true when the bus lanes share the road with general traffic and the lane is reassigned from general traffic to a dedicated bus lane.
The 2017 MWCOG Bus Lane Enforcement study reported five components of bus lane management:
For more information, see: https://www.mwcog.org/assets/1/28/10062017_-_Item_12_-_DO_NOT_PRINT_-_Bus_Lane_Enforcement_Study_Final_Report.pdf

## Slide 53
Challenges of Bus Priority – Approval
TPB Bus Priority Synthesis
November 2020
In order to implement any bus priority infrastructure, the program must be approved by relevant stakeholders, including the city government, the transit agency, the streets department, and any impacted community members/organizations.
Taking away an existing parking or travel lane can be politically unpopular and creating additional right-of-way can be expensive.
In order to manage public/political dynamics, it is important to engage stakeholders and the public early and often throughout the planning and implementation process
Photo Credit: Transportation planning public meeting advertisement
(North Central Texas Council of Governments)
For more information, see: https://nacto.org/docs/usdg/tcrp_rpt_90_implementation_guidelines_volume_2_levinson.pdf

## Slide 54
Key information from Peers on benefits and costs of bus priority

## Slide 55
5.5-mile network of dedicated bus lanes in Downtown Baltimore on nine streets
Implemented in 2017 with BaltimoreLink network redesign
Resulted in:
  Average travel time savings of 9.3 percent per corridor
  Average of less than one-minute increases to general traffic
  Reduction of bus related safety incidents by 12 percent
Enforcement issues limited initial effectiveness
BaltimoreLink Transit Priority Initiative
TPB Bus Priority Synthesis
November 2020
Source: Dedicated Bus Lanes Before and After Study, MDOT MTA, February 2019, https://s3.amazonaws.com/mta-website-staging/mta-website-staging/files/System%20Information/DBL_Report_022019.pdf
Photo Source: BaltimoreLink Dedicated Bus Lanes (MDOT MTA, Before and After Study)

## Slide 56
Loop Link is a network of dedicated bus lanes within Chicago’s downtown
Features include
  Dedicated lanes
  Enhanced stations
  Raised platform boarding
Intended to improve travel flow on several key corridors
Has had limited success since implementation due to lack of enforcement
Loop Link cost over $30 million to implement.
Chicago Loop Link
TPB Bus Priority Synthesis
November 2020
Loop Link Station, (NACTO/Flickr)
Source: Blair Kamin, “Chicago’s Loop Link not exactly rapid, but a step in the right direction,” Chicago Tribune, January 9, 2016. https://www.chicagotribune.com/columns/ct-loop-link-review-kamin-met-0110-20160108-column.html

## Slide 57
BRT-lite route connecting Minneapolis and St. Paul
Features include:
  Enhanced stations
  Transit Signal Priority
  Off-board fare payment
  Real-time trip information
Corridor ridership grew 32 percent in first year of operation
Average A Line speed is 19.7 miles per hour, compared to 13.4 miles per hour for local bus routes
Implementation cost about $27 million
Minneapolis-St. Paul METRO A Line
TPB Bus Priority Synthesis
November 2020
Sources: “Metro Transit A Line 2017 Snap Shot,” Metro Transit, https://www.metrotransit.org/Data/Sites/1/media/abrt/aline/11-002-01-18_aline_factsheet.pdf
Metropolitan Area Transit Finance Report, Metropolitan Council, October 2018, https://metrocouncil.org/Transportation/Publications-And-Resources/Finance/Metropolitan-Area-Transit-Finance-Report,-2018.aspx
“A Line Project FAQs,” Metro Transit, https://www.metrotransit.org/a-line-project-faqs#:~:text=The%20total%20cost%20of%20the,technology%20and%20fare%20collection%20elements&text=%244%20million%20to%20design%20the%20stations%2C%20roadway%20improvements%20and%20technology
Source: METRO A Line Station, (Metro Transit/University of Minnesota Center for Transportation Studies)

## Slide 58
MTA offers SBS on 16 routes on high ridership corridors.
SBS routes feature BRT elements
  Off-board fare payment
  TSP
  Consolidated stops
On average, SBS is 27 percent faster than local/limited routes
Implementing and operating SBS averages about $10 million per route
The first four SBS routes improved travel time by an average of 19 percent
New York City Select Bus Service (SBS)
TPB Bus Priority Synthesis
November 2020
Source: Better Bus Action Plan. New York City Department of Transportation. 2019. https://www1.nyc.gov/html/brt/downloads/pdf/better-buses-action-plan-2019.pdf
Source: Select Bus Services Launch M86 (NYC DOT/Flickr)

## Slide 59
The 14th Street Busway bans private vehicles from making through trips on 14th Street between 6:00 A.M. and 10:00 P.M. daily
Pilot began in October 2019 and was made permanent in June 2020
Bus travel speeds increased by 24 percent on the corridor
Ridership increased 30 percent on the corridor
Shifting local traffic to adjacent roads has had limited impacts on travel speeds
New York City 14th Street Busway
TPB Bus Priority Synthesis
November 2020
Sources: “14th Street Busway,” NYC DOT, https://www1.nyc.gov/html/brt/html/routes/14th-street.shtml
“Banning Cars on 14th Street, No Problem,” Inrix, https://inrix.com/blog/2019/10/nyc-busway/
Source: 14th Street Transitway (MTA/Flickr)

## Slide 60
Metro Rapid is LA Metro’s express bus service
Operates in mixed traffic with distinctive branding
TSP led to an estimated 25 percent reduction in bus travel times compared to travel without TSP
Operating cost savings of $6.67 per bus per hour
  $66.77 per bus per day, $24k per bus per year
Implementing TSP cost $13,500 per signalized intersection
Los Angeles Metro Rapid
TPB Bus Priority Synthesis
November 2020
Source: White Paper #2: Strategic Considerations, Bus Transformation Project, 2019, https://bustransformationproject.com/wp-content/uploads/2019/01/White-Paper-2_FINAL.pdf
Source: Metro Rapid, Los Angeles (NACTO/ Flickr)

## Slide 61
TriMet implemented TSP capabilities at over 250 intersections in Portland
TSP impacts:
  Reduced bus travel time by 10 percent
  Reduced travel time variability by 19 percent
Improvements saved the agency over $13 million over eight years
Equipping 250 intersections with TSP cost approximately $4.5 million
Portland TriMet TSP Program
TPB Bus Priority Synthesis
November 2020
Source: White Paper #2: Strategic Considerations, Bus Transformation Project, 2019, https://bustransformationproject.com/wp-content/uploads/2019/01/White-Paper-2_FINAL.pdf
Source: Transit Priority Signal (TriMet/Flickr)

## Slide 62
MuniForward is SFMTA’s initiative to create a safer, more reliable transit experience
A transit lane on Church Street eliminated congestion-related delays for buses without significant impacts to drivers
The red paint treatment reduced transit lane violations by 50 percent compared to non-colored transit-only lanes
Restriping and repainting the Church Street corridor cost about $280,000 per mile
San Francisco MuniForward Transit Priority Projects
TPB Bus Priority Synthesis
November 2020
Sources: Implementation Workbook, Muni Forward, San Francisco Municipal Transportation Agency, 2015, https://www.sfmta.com/sites/default/files/reports-and-documents/2018/04/muni_forward_implementation_workbook_v16.3_web.pdf
Church Street Transit Lanes Final Report, SFMTA, https://www.sfmta.com/sites/default/files/agendaitems/2015/6-2-15%20Item%2012%20%20Church%20St.%20Rapid%20Pilot%20-%20Final%20Report_1.pdf
Source: Muni’s Red Carpet (NACTO/Flickr)

## Slide 63
Seattle RapidRide is King County Metro’s BRT-lite network
RapidRide serves 67,000 riders every weekday, a 70 percent increase compared to the previous service
Peak hour travel is 20 percent faster than the previous service
Seattle RapidRide
TPB Bus Priority Synthesis
November 2020
Sources: RapidRide Expansion, King County Metro, https://kingcounty.gov/depts/transportation/metro/programs-projects/fares-routes-and-service/rapidride-expansion.aspx; Transit Master Plan, City of Seattle Department of Transportation, 2016, https://www.seattle.gov/Documents/Departments/SDOT/TransitProgram/TMPSupplmtALL2-16FINAL.pdf
King County Metro RapidRide Performance Evaluation Report, King County Metro, http://metro.kingcounty.gov/am/reports/2014/rapidride-performance-evaluation-report-2014.pdf
Top: RapidRide Station (SDOT/Flickr)
Bottom: Rapid Ride Station (King County Metro/King County Metro RapidRide Performance Evaluation Report)

## Slide 64
RapidRide’s cost per passenger was 21 percent less than King County Metro’s local service in 2013
TSP, signal timing, and ITS infrastructure investments combined cost between $1.76 million and $2.78 million per route to implement
Implementing real-time infrastructure cost $400,000 to $1 million per route
Investments in off-board fare readers cost between $95,000 to $300,000 per route
Seattle RapidRide
TPB Bus Priority Synthesis
November 2020
Source: Performance Metrics (King County Metro/ King County Metro RapidRide Performance Evaluation Report)

## Slide 65
Viva, express bus service, opened in 2005 and construction of dedicated “rapidways” began in 2011 using P3 model
York transit ridership increased by 26 percent between 2005 and 2013
Key to Viva’s success is its marketing campaign
  Focus on selling a lifestyle
The full network of transitways will cost approximately 1.7 billion Canadian dollars ($1.2 billion USD)
York Region (Toronto) Viva BRT
TPB Bus Priority Synthesis
November 2020
Source: Viva BRT Station (Ontario Municipal Housing and Affairs/Flickr)
YRT/Viva Bus Rapid Transit, Metrolinx, http://www.metrolinx.com/en/greaterregion/projects/york-viva-bus-rapid-transit.aspx
Jesse Thomas, “Suburban Toronto’s Viva offers lessons for Montgomery BRT,” Greater Greater Washington, August 27, 2013, https://ggwash.org/view/32171/suburban-torontos-viva-offers-lessons-for-montgomery-brt
YRT/Viva Bus Rapid Transit, Metrolinx, http://www.metrolinx.com/en/greaterregion/projects/york-viva-bus-rapid-transit.aspx

## Slide 66
Ongoing and future bus priority projects in the ncr

## Slide 67
Near Term and Planned Bus Priority Projects in the Region
TPB Bus Priority Synthesis
November 2020

## Slide 68
The NCR is moving forward in improving bus reliability and efficiency
  The Bus Transformation Project (BTP) laid out strategies and action steps to transform the NCR’s bus system to provide fast, frequent, reliable, and affordable bus system
  Numerous projects under construction and in early planning phases are helping push the region towards the BTP’s vision
  Metroway (BeoyondDC/Flickr)
TPB Bus Priority Synthesis
November 2020

## Slide 69
Near Term Bus Priority Projects
TPB Bus Priority Synthesis
November 2020

## Slide 70
The project includes:
  Dedicated bus bike and bus lanes
  Bus stop consolidation
  Parking limitations
Expected to improve performance of the DC Circulator and Metrobus Routes 52, 56, and 59, which combined carry over 15,500 travelers daily
The demonstration project began construction in Summer 2020 and will be implemented for one year
14th Street Bus Lane Decongestion Project
TPB Bus Priority Synthesis
November 2020
Source: Sample Section on 14th Street NW (DDOT/https://ddot.dc.gov/node/1444606)

## Slide 71
WMATA serves over 20,000 passengers per weekday on 16th Street NW
The S9 MetroExtra limited-stop service, signal timing optimization, and transit signal priority implemented on the corridor prior to 2016
The 16th Street Bus Priority Study (2016) analyzed:
  Potential service
  Physical and operational improvements
16th Street Bus Lane Project
TPB Bus Priority Synthesis
November 2020
Source: 16th Street NW Bus Lanes Project, https://www.16thstreetnwbus.com/

## Slide 72
The 2016 study recommended:
  Queue jumps
  All-door boarding
  Off-board fare payment
  Bus stop consolidation
  Dedicated bus lanes
  Parking limitations
Improvements expected to reduce travel times in both directions by two to five minutes compared to the existing service
Construction on the 16th Street corridor is expected to begin in Fall 2020
16th Street Bus Lane Project
TPB Bus Priority Synthesis
November 2020
Source: 16th Street NW Bus Lanes Project, https://www.16thstreetnwbus.com/

## Slide 73
Montgomery County the Countywide Transit Corridors Functional Master Plan recommended 11 BRT corridors
  Georgia Avenue North (1)
  Georgia Avenue South (2)
  MD 355 North (3)
  MD 355 South (4)
  New Hampshire Avenue (5)
  North Bethesda Transitway (6)
  Randolph Road (7)
  University Boulevard (8)
  US 29 (9)
  Veirs Mill Road (10)
  Corridor City Transitway (CCT)
Montgomery County Bus Rapid Transit
TPB Bus Priority Synthesis
November 2020
Source: Montgomery Planning, Countywide Transit Corridors Functional Faster Plan, Montgomery County, MD, https://montgomeryplanning.org/planning/transportation/transit-planning/countywide-transit-corridors-functional-master-plan/

## Slide 74
US 29 FLASH opened on October 14, 2020 and features:
  Bus-on-shoulder lanes between Burtonsville and Tech Road
  TSP installed at 15 intersections
US 29 FLASH is expected to reduce travel time by 22 to 35 percent on the corridor compared to existing local bus service
US 29 FLASH is also expected to result in over $250 million of economic net benefit
Montgomery County Bus Rapid Transit
TPB Bus Priority Synthesis
November 2020
Source: FLASH, https://www.ridetheflash.com/us29/.
MCDOT US 29 BRT Project Summary, https://www.ridetheflash.com/wp-content/uploads/2018/04/US_29_March2018_Open_Houses_Boards.pdf

## Slide 75
Planned Bus Priority Projects
TPB Bus Priority Synthesis
November 2020

## Slide 76
Pedestrians, cyclists, and people on buses make up the majority of travelers on K Street NW
The K Street Transitway will operate between 12th and 21st Streets NW, consisting of:
  A two-way dedicated busway separated by medians, running in the center of K Street
  General purpose travel lanes
  Off-peak parking lanes
  Dedicated cycle track in each direction
K Street Transitway
TPB Bus Priority Synthesis
November 2020
Source: K Street Transitway (DDOT/https://ddot.dc.gov/page/k-street-transitway)

## Slide 77
Busway designed to carry at least 13 bus routes with 55 buses per hour per direction during peak periods
Construction expected to begin in 2022, with the Transitway opening in 2024
Once complete, travel times on the Transitway are expected to improve by 30 percent compared to existing conditions
K Street Transitway
TPB Bus Priority Synthesis
November 2020
Source: K Street Transitway (DDOT/https://ddot.dc.gov/page/k-street-transitway)
21st Street NW to 17th Street NW

## Slide 78
Pennsylvania Avenue is a wide boulevard and major thoroughfare
The 30S Metrobus operates on the Avenue, carrying over 11,000 passengers daily
Up to 18 buses per hour operate in the AM peak on the corridor, and up to 24 buses operate in the PM Peak
Bus reliability is poor; the Metrobus Report Card graded the corridor an “F” for scheduled adherence
Pennsylvania Avenue Southeast Corridor Study
TPB Bus Priority Synthesis
November 2020
Source: Pennsylvania Avenue Southeast Corridor Study, https://www.pennavese.com/

## Slide 79
Pennsylvania Avenue Southeast Corridor Study
TPB Bus Priority Synthesis
November 2020
Source: Pennsylvania Avenue Southeast Corridor Study, https://www.pennavese.com/
Alternatives analysis is currently underway to improve multimodal mobility on the corridor
Notes: DDOT developed alternatives for the corridor which aim to improve multimodal mobility on the corridor

## Slide 80
Envision Route 7 is BRT project that connects the Mark Center in Alexandria to Tysons through Bailey’s Crossroads, Seven Corners, and Falls Church
The initial running way assumptions and station locations are currently being updated and right-of-way prioritization defined
Future phases will focus on traffic impacts and benefits, and environmental and detailed design efforts
Envision Route 7
TPB Bus Priority Synthesis
November 2020
Source: NVTC, Envision Route 7, http://www.novatransit.org/programs/route7/

## Slide 81
Adding to Metroway, and completing a network of bus priority corridors, the City of Alexandria has planned Corridors B and C
Corridor B, on Duke Street and Eisenhower Avenue, would connect Alexandria to Fairfax County to the west
Corridor C, on Van Dorn/Beauregard Street has the potential to tie to Columbia Pike, Fairfax County, and the Pentagon area
City of Alexandria Transitway Corridors
TPB Bus Priority Synthesis
November 2020
Source: City of Alexandria Transitway Corridors Feasibility Study: https://www.alexandriava.gov/uploadedFiles/tes/info/Final_Transitways_Report_2012-10-19_forscreen(2).pdf

## Slide 82
Proposed BRT line on Route 1 between Interstate 495 and Woodbridge
Route would operate on an exclusive transitway with off-board fare payment and level boarding
Preliminary studies estimate travel time savings of up to nine minutes on the corridor
Embark Richmond Highway Bus Rapid Transit
TPB Bus Priority Synthesis
November 2020
Source: “Embark Richmond Highway – Plan Amendment 2015-IV-MV1; Adopted Amendment No. 2017-10 & No. 2017 P-02,” Fairfax County, VA, https://www.fairfaxcounty.gov/planning-development/embark-richmond-highway
“Richmond Highway Bus Rapid Transit (BRT)”, Fairfax County, Virginia, https://www.fairfaxcounty.gov/transportation/richmond-hwy-brt. Route 1 Multimodal Alternatives Analysis. Virginia Department of Rail and Public Transportation and Virginia Department of Transportation, http://www.drpt.virginia.gov/media/1591/route-1-final-report-with-appendices-february-2015.pdf.

## Slide 83
Presenter Name | mwcog.org/tpb

## Slide 84
Additional Slides on TIGER Projects
TPB Bus Priority Synthesis
November 2020

## Slide 85
16th Street NW, DC
TPB Bus Priority Synthesis
November 2020
Bus priority treatments included:
  TSP at 31 intersections
  Queue jump at one intersection
Routes on the corridor with reported performance measures are:
  WMATA Routes S1, S2, S4, and S9

## Slide 86
16th Street NW, DC
TPB Bus Priority Synthesis
November 2020
Reported measures:
  Transit Service Level
  Passenger Counts
  Average Load
  On-Time Performance
  Vehicle Travel Time for Corridor
  Passenger Miles for Corridor
  Passenger Hours of Travel for Corridor
  Transit Rider Characteristics
Photo Source: Bus queue jump signal, 16th St DC
(BeyondDC/Flickr)

## Slide 87
16th Street NW, DC
TPB Bus Priority Synthesis
November 2020
Route S9 ridership has increased significantly from 2011 to 2018
Ridership on routes S2 and S4 showed a change similar to other Metrobus routes in the sector
Chart: Average Monthly Weekday Metrobus Ridership (2011 to 2018)
| 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018
S1 | 40707.9167 | 42336.3333 | 44696.0833 | 41524.5833 | 42925 | 40840.6667 | 42228.9167 | 41202.3333
S2, S4 | 300615.0833 | 309857.9167 | 301911.25 | 295422.75 | 277763.75 | 264308 | 220232.5 | 173135.5833
S9 | 56651.5 | 61537.9167 | 79437.25 | 77788.8333 | 75648.9167 | 76373.5833 | 96069.4167 | 121050.0833
Central DC | 1666753.5833 | 1705182.6667 | 1752089.8333 | 1744354.25 | 1713629.8333 | 1638459.9167 | 1544997.9167 | 1482135.25

## Slide 88
16th Street NW, DC
TPB Bus Priority Synthesis
November 2020
Route S9 performed at or above WMATA’s 79% on-time standard in all periods, except for the afternoon peak
On-time performance declined in the morning and afternoon peak periods, while slightly increasing midday
Chart: WMATA Route S9 Annual Weekday OTP
| 6:00 AM - 9:00 AM | 9:00 AM - 3:00 PM | 3:00 PM - 7:00 PM | 7:00 PM - 11:00 PM
Before | 0.8895 | 0.83317 | 0.81333 | 0
2nd After Report | 0.7947 | 0.8616 | 0.7643 | 0.8595
Before data is from January 2010 to June 2011 2nd After Report data is from January 2018 to December 2018

## Slide 89
Georgia Avenue NW, DC
TPB Bus Priority Synthesis
November 2020
Bus priority treatments included:
  0.3 mi of dedicated bus lanes
  TSP at 57 intersections
  Queue jump at 3 intersection
Routes on the corridor with reported performance measures are:
  WMATA Routes 70, 74, and 79

## Slide 90
Georgia Avenue NW, DC
Agenda TPB Bus Priority Synthesis
November 2020
Reported measures:
  Transit Service Level
  Transit Passenger Counts
  On-time Performance
  Passenger Counts/Average Load
  Vehicle Travel Time for Corridor
  Transit Passenger Miles and Hours of Travel
Photo Source: Georgia Avenue red-painted bus lane
(BeyondDC/Flickr)

## Slide 91
Georgia Avenue NW, DC
TPB Bus Priority Synthesis
November 2020
Ridership on corridor peaked in 2014 and routes experienced similar trends to other bus routes in the area
Levels of ridership on Routes 70, 74, and 79 in 2018 have maintained their 2011 levels better than the combined sector
Chart: Average Monthly Weekday Metrobus Ridership (2011 to 2018)
| 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018
70 | 206816.3333 | 234641.4167 | 236929.9167 | 243191.3333 | 242818 | 236633.9167 | 231778.25 | 223348.1667
74 | 22588.75 | 30726 | 32446.1667 | 35459.4167 | 32641.3333 | 29062.5 | 26249.9167 | 22947.8333
79 | 134638.3333 | 144291.6667 | 148838.9167 | 158749.75 | 154150.4167 | 144832.3333 | 134503.6667 | 124884.9167
Central DC | 1666753.5833 | 1705182.6667 | 1752089.8333 | 1744354.25 | 1713629.8333 | 1638459.9167 | 1544997.9167 | 1482135.25

## Slide 92
Georgia Avenue NW, DC
TPB Bus Priority Synthesis
November 2020
On-time performance increased midday and during the evening
None of the periods had average performance higher than WMATA’s 79 percent on-time standard for 2018
Chart: WMATA Route 79 Annual Weekday OTP
| 4:00 AM - 6:00 AM | 6:00 AM - 9:00 AM | 9:00 AM - 3:00 PM | 3:00 PM - 7:00 PM | 7:00 PM - 11:00 PM | 11:00 PM - 4:00 AM
Before | 0.8175 | 0.7809 | 0.6896 | 0.6321 | 0.6676 | 0.6586
2nd After Report | 0.6061 | 0.7648 | 0.7673 | 0.5708 | 0.6906
Before data is from January 2010 to March 2011 2nd After Report data is from January 2018 to December 2018

## Slide 93
Wisconsin Avenue, DC
TPB Bus Priority Synthesis
November 2020
Bus priority treatments included TSP at 39 intersections
Routes on the corridor with reported performance measures are:
  WMATA Routes 37, 39, 30N, 30S, 31, 32, 33, 34, 36, and M6

## Slide 94
Wisconsin Avenue, DC
TPB Bus Priority Synthesis
November 2020
Reported measures:
  Transit service level
  Transit passenger counts
  On-time performance
  Passenger counts / Average Load
  Vehicle travel time for corridor
  Transit passenger miles and hours of travel
On-time performance increased during the morning peak slightly, while midday presented significant OTP increase
Chart: WMATA Routes 37 and 39 Annual Weekday OTP
| 6:00a-9:00a | 9:00a-3:00p | 3:00-7:00p | 7:00p-11:00p
Before Report (2010) | 72.6875 | 47.0875 | 65.125 | 0
1st After Report (2016) | 77.34 | 72.42 | 55.54 | 71.55
2nd After Report (2018) | 72.74 | 68.79 | 56.51 | 72.26
Before data is from January 2010 to December 2010 1st After Report data is from December 2015 to December 2016 2nd After Report data is from December 2017 to December 2018

## Slide 95
US 1 - Transitway, VA
TPB Bus Priority Synthesis
November 2020
TIGER funded the construction of one 0.8-mile segment of transitway
This project implemented segment B of the bus transitway
Routes on the corridor with reported performance measures are WMATA Routes 9A, 10S, and Metroway

## Slide 96
US 1 - Transitway, VA
TPB Bus Priority Synthesis
November 2020
Reported measures:
  Transit Service Level
  Passenger Counts
  Average Load
  On-Time Performance
  Vehicle Travel Time for Corridor
  Passenger Miles for Corridor
  Passenger Hours of Travel for Corridor
  Transit Rider Characteristics
Photo Source: Metroway BRT
(BeyondDC/Flickr)

## Slide 97
US 1 - Transitway, VA
TPB Bus Priority Synthesis
November 2020
Overall, on-time performance has increased since 2010, due to the high on-time performance rates of the Metroway
On-time performance dipped slightly from 2015 to 2016
Still, OTP for the routes on the corridor exceeds WMATA’s standards
Chart: Average Annual Weekday OTP
| 4:00a-6:00a | 6:00a-9:00a | 9:00a-3:00p | 3:00p-7:00p | 7:00p-11:00p | 11:00p-4:00a
Before Report | 0.915 | 0.872 | 0.848 | 0.775 | 0.86 | 0.84
1st After Report | 0.96552 | 0.9204 | 0.92409 | 0.87664 | 0.91739 | 0.92537
2nd After Report | 0.9481 | 0.9092 | 0.904 | 0.8367 | 0.8891 | 0.8566
Before data is from January 2010 to December 2010 1st After Report data is from August 2014 to July 2015 2nd After Report data is from August 2015 to July 2016

## Slide 98
VA 7 (Leesburg Pike), VA
TPB Bus Priority Synthesis
November 2020
Bus priority treatments included TSP at 25 intersections
Routes on the corridor with reported performance measures are:
  WMATA Routes 28X, 28A, 28F, and 28G

## Slide 99
VA 7 (Leesburg Pike), VA
TPB Bus Priority Synthesis
November 2020
Reported measures:
  Transit service level
  Transit passenger counts
  On-time performance
  Passenger counts / Average Load
  Vehicle travel time for corridor
  Transit passenger miles and hours of travel
On-time performance increased during the morning peak significantly, while decreasing during the afternoon peak
Chart: Average Annual Weekday OTP
| 4:00 AM - 6:00 AM | 6:00 AM - 9:00 AM | 9:00 AM - 3:00 PM | 3:00 PM - 7:00 PM | 7:00 PM - 11:00 PM | 11:00 PM - 4:00 AM
Before Report | 0.6333 | 0.878
1st After Report | 0.92726 | 0.90778 | 0.86727 | 0.83176 | 0.71481 | 0.82908
2nd After Report | 0.93066 | 0.85992 | 0.85191 | 0.65841 | 0.82214 | 0.83007
Before data is from January 2010 to December 2010 1st After Report data is from December 2015 to December 2016 2nd After Report data is from December 2016 to December 2017

## Slide 100
Van Dorn – Pentagon, VA
TPB Bus Priority Synthesis
November 2020
Bus priority treatments included TSP at 9 intersections and 2 queue jumps
Routes on the corridor with reported performance measures are:
  WMATA Routes 7A, 7F, 7W, and 25B
  DASH Routes AT1 and AT5

## Slide 101
Van Dorn – Pentagon, VA
TPB Bus Priority Synthesis
November 2020
Reported measures:
  Transit service level
  Transit passenger counts
  On-time performance
Passenger counts decrease in most routes, as well as in the sector
On-time performance increased for all WMATA routes in the corridor and met the 79% target on weekdays at all periods from September 2017 to August 2018
Chart: Average Monthly Ridership
| 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018
25B | 31991.1667 | 31903.3333 | 28938.6667 | 29787.4167 | 38248 | 42319.5833 | 40645.8333 | 37626.8333
7A | 29521.5833 | 30459.5833 | 31210.3333 | 33663.1667 | 32383.75 | 29652.6667 | 26749.1667 | 24601.1667
7F | 21593.6667 | 21962.9167 | 21176.9167 | 20445.0833 | 18959 | 17154.3333 | 16821.3333 | 14477.9167
7W | 13199.8333 | 12069.6667 | 11937.5833 | 11408.9167 | 11294.9167 | 10408.3333 | 10092 | 12206.9167
7X | 8148.9167 | 7387.9167 | 7023.25 | 7411.4167 | 7137.75 | 6753.75 | 6932
Central & Eastern NOVA | 1169264.0833 | 1191507.4167 | 1180797 | 1188170.4167 | 1166144.5 | 1119775.4167 | 1070239.3333 | 991957.8333

## Slide 102
T. Roosevelt Bridge to K Street NW, DC
TPB Bus Priority Synthesis
November 2020
Bus priority treatments included TSP at 68 in Central DC
Reported measures:
  Transit service level
  Passenger counts
Routes on the corridor with reported performance measures are:
  WMATA routes 3Y, 7Y, 16Y
  OmniRide Manassas and Gainesville routes
  Loudoun County Purcellville, Leesburg, Dulles North and South, and Ashburn North runs

## Slide 103
T. Roosevelt Bridge to K Street NW, DC
TPB Bus Priority Synthesis
November 2020
WMATA routes ridership on the corridor in 2018 is greater than in 2011
Routes and sector ridership trends are mostly similar
Chart: Average Monthly Weekday Ridership
| 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018
3Y | 7546.4167 | 8806.9167 | 9174.8333 | 8929.8333 | 8984.3333 | 11267.0833 | 10258.3333 | 9346.5
Western NOVA Sector | 17571.2707 | 17738.7806 | 17903.1954 | 21388.7007 | 22094.9048 | 20558.2116 | 19471.9737 | 19650
Chart: Average Monthly Weekday Ridership
| 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018
7Y | 23215.1667 | 25400.3333 | 26658.6667 | 26383.6667 | 28524.5 | 27261.75 | 24853.75 | 24097.75
Eastern NOVA Sector | 10780.9873 | 11363.8778 | 11222.0896 | 10782.0094 | 10766.0154 | 11106.0845 | 11520.6325 | 12017
Chart: Average Monthly Weekday Ridership
| 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018
16Y | 27714.4167 | 29757.8333 | 34300.75 | 35296.3333 | 36249.0833 | 37659.9167 | 37405.8333 | 32905.6667
Central NOVA Sector | 18129.5891 | 17853.3955 | 17135.0726 | 17602.4101 | 19616.3205 | 20495.2724 | 19232.8576 | 21311

## Slide 104
14th Street Bridge to K Street NW, DC
TPB Bus Priority Synthesis
November 2020
Bus priority treatments included TSP at 68 in Central DC
Reported measures are transit service level and passenger counts
Routes on the corridor with reported performance measures are:
  WMATA routes 5A, 11Y, 16C, 16E
  OmniRide Dale City, Lake Ridge, South Route 1, and Montclair routes
  Loudoun Co. Purcellville, Leesburg, Dulles North, and Dulles South runs

## Slide 105
14th Street Bridge to K Street NW, DC
TPB Bus Priority Synthesis
November 2020
Ridership on WMATA routes 11Y and 16C has mostly followed the sector’s trends and increased
WMATA route 5A was significantly impacted by Silver Line Metrorail opening in 2014