## Slide 1
December 12th, 2016
Water-Quality Monitoring in an
Urban Watershed:
The Influence of Septic Systems on
Nitrate Concentrations
and Spatial Patterns
This information is preliminary and is subject to revision. It is being provided to meet the need for timely best science. The information is provided on the condition that neither the U.S. Geological Survey nor the U.S. Government shall be held liable for any damages resulting from the authorized or unauthorized use of the information.
Jimmy Webber
jwebber@usgs.gov
Ken Hyer
kenhyer@usgs.gov
John Jastram
jdjastra@usgs.gov
JK Böhlke
jkbohlke@usgs.gov
Judy Denver
jmdenver@usgs.gov
Michael Langland
Langland@usgs.gov

## Slide 2
Sampling location included in
Fairfax County monitoring network
Sampling location within Difficult Run
Difficult Run nr Great Falls, VA
USGS: 01646000
Water-Quality Monitoring in an
Urban Watershed:
The Influence of Septic Systems on
Nitrate Concentrations
and Spatial Patterns

## Slide 3
Difficult Run:
Spatial Water-Quality Data
1
100
Percent Impervious
Reston
Tysons
Corner
Fairfax City
1
1Percent of impervious land cover from 2011 NLCD
Difficult Run nr Great Falls, VA
USGS: 01646000
Hyer and others, 2016

## Slide 4
Difficult Run:
Specific Conductance Data
1
100
Percent Impervious
Reston
Fairfax City
165 – 210
211 – 255
256 – 300
301 – 345
346 – 390
Specific Conductance,
in μS/cm
Tysons
Corner
2Specific conductivity data based on the average of 6 synoptic events between 2011 and 2015.
1
1Percent of impervious land cover from 2011 NLCD
2
Difficult Run nr Great Falls, VA
USGS: 01646000
2
1
Hyer and others, 2016

## Slide 5
Open Space
Estate Residential
Low-Density Residential
Medium-Density Residential
High-Density Residential
Outside Jurisdiction
High-Intensity Commercial
Industrial
Roads
Low-Intensity Commercial
Unknown
LANDUSE
Difficult Run:
Landuse
1
1Landuse from Fairfax County GIS data, 2014.
Difficult Run nr Great Falls, VA
USGS: 01646000

## Slide 6
Difficult Run:
Nitrate-N Concentrations
Open Space
Estate Residential
Low-Density Residential
Medium-Density Residential
High-Density Residential
Outside Jurisdiction
High-Intensity Commercial
Industrial
Roads
Low-Intensity Commercial
Unknown
LANDUSE
0.0 – 1.0
1.1 – 2.0
2.1 – 3.0
3.1 – 4.0
4.1 – 5.0
Nitrate-N,
in mg/L
Captain Hickory Run
2Nitrate-N data based on the average of 6 synoptic events between 2011 and 2015.
1
1Landuse from Fairfax County GIS data, 2014.
2
Difficult Run nr Great Falls, VA
USGS: 01646000
Hyer and others, 2016

## Slide 7
Captain Hickory Run:
Nitrate-N Concentrations
0.0 – 2.0
2.1 – 4.0
4.1 – 6.0
6.1 – 8.0
8.1 – 10.0
Nitrate-N,
in mg/L
2Nitrate-N data collected between 2012 and 2016.
Watershed Area = 1.38 mi2
Historic Agricultural Practices?
Wastewater?
Fertilizer Application?
2
Preliminary Information-Subject to Revision. Not for Citation or Distribution

## Slide 8
Captain Hickory Run
Difficult Run:
Nitrogen Sources
1Nitrate-N data based on the average of 6 synoptic events between 2011 and 2015.
Conventional Septic System
Alternative Septic System
2GIS data of properties served by septic systems provided by Fairfax County, May 2015.
1
2
2
2
0.0 – 1.0
1.1 – 2.0
2.1 – 3.0
3.1 – 4.0
4.1 – 5.0
Nitrate-N,
in mg/L
1
Geochemically Similar
Little Difficult Run
Difficult Run nr Great Falls, VA
USGS: 01646000
Hyer and others, 2016

## Slide 9
Fairfax County:
Nitrogen Sources
1Small watershed nitrate-N data based on the average of 6 synoptic events between 2011 and 2015. Fairfax county nitrate-N data based on the average of baseflow samples collected between 2008 and 2015.
Conventional Septic System
Alternative Septic System
2GIS data of properties served by septic systems provided by Fairfax County, May 2015.
1
2
2
2
0.0 – 1.0
1.1 – 2.0
2.1 – 3.0
3.1 – 4.0
4.1 – 5.0
Nitrate-N,
in mg/L
1
Sampling location included
in Fairfax County monitoring network
Sampling location included
in Small Watershed study
(within Difficult Run)
Captain Hickory Run
SF Little Difficult Run
Hyer and others, 2016
Elevated nitrate concentrations appear to be caused by high septic system density based on:
(1) nitrate isotopes, (2) monthly nitrate concentrations, (3) land-use data, and (4) chemical indicators of wastewater.

## Slide 10
Fairfax County:
Nitrogen Sources
1
Baseflow Conditions
Stormflow Conditions
No evidence of seasonally elevated nitrate concentrations that might be attributed to the runoff of lawn fertilization in the spring and fall.
Hyer and others, 2016

## Slide 11
Fairfax County:
Nitrogen Sources
0
0.1 – 1.0
1.1 – 4.0
4.1 – 7.0
7.1 – 10.0
Ratio of estimated
septic1/fertilizer2 TN load
10.1 – 13.0
Primarily Fertilizer
Primarily Septic
2Fertilizer load computed from an estimated fertilizer application (Law and others 2004) and fertilizer-N leaching rate (Petrovic, 2008).
1Septic load computed from an estimated per capita septic system loading rate (Maizel and others, 1997).
Preliminary Information-Subject to Revision. Not for Citation or Distribution
The mass of nitrogen available from septic system leachate could be approximately an order of magnitude greater than that from fertilizer.

## Slide 12
2
2
Difficult Run:
Nitrogen Sources
Watershed
Difficult Run
Smith Creek
Upper Chester
Septic
Art. fert.
Forest soils
Common delta N-15 values of nitrate sources:
Manure
Septic
Art. fert.
Forest soils
**Typical range of error, 2-sigma
Common delta N-15 values of nitrate sources:
Sites with elevated nitrate concentrations have δ15N values similar to those commonly attributed to sewage or septic system sources.
Hyer and others, 2016

## Slide 13
Captain Hickory Run:
Indicators of Wastewater: 4-nonylphenol
0.0 – 2.0
2.1 – 4.0
4.1 – 6.0
6.1 – 8.0
8.1 – 10.0
Nitrate-N,
in mg/L
2Nitrate-N data collected between 2012 and 2016.
Watershed Area = 1.38 mi2
2
Site 34
Site 33
Site 25
Site A
Site B
Site C
Site D
March 2016
June 2016
This information is preliminary and is subject to revision. It is being provided to meet the need for timely best science. The information is provided on the condition that neither the U.S. Geological Survey nor the U.S. Government shall be held liable for any damages resulting from the authorized or unauthorized use of the information.

## Slide 14
Captain Hickory Run:
Indicators of Wastewater: HF-183
0.0 – 2.0
2.1 – 4.0
4.1 – 6.0
6.1 – 8.0
8.1 – 10.0
Nitrate-N,
in mg/L
2Nitrate-N data collected between 2012 and 2016.
Watershed Area = 1.38 mi2
2
Site 34
Site 33
Site 25
Site A
Site B
Site C
Site D
March 2016
June 2016
July 2014
Below Detection
This information is preliminary and is subject to revision. It is being provided to meet the need for timely best science. The information is provided on the condition that neither the U.S. Geological Survey nor the U.S. Government shall be held liable for any damages resulting from the authorized or unauthorized use of the information.

## Slide 15
Difficult Run:
Nitrate-N Trend
Difficult Run nr Great Falls, VA
USGS: 01646000
Hyer and others, 2016
1Nitrate-N data based on the average of 6 synoptic events between 2011 and 2015.
2GIS data of properties served by septic systems provided by Fairfax County, May 2015.
Nitrate concentrations and loads have increased at the Difficult Run streamgage between 1985-20143.
3Trend analysis using Weighted Regressions on Time, Discharge, and Season (WRTDS). Results available online: http://cbrim.er.usgs.gov/

## Slide 16
Difficult Run:
Nitrogen Load from Septic
Difficult Run nr Great Falls, VA
USGS: 01646000
1Nitrate-N data based on the average of 6 synoptic events between 2011 and 2015.
2GIS data of properties served by septic systems provided by Fairfax County, May 2015.
Based on base flow sampling results, approximately 5% of the total nitrogen load leaving the watershed may be contributed by septic systems:
Water Year 2013: 9,000 lbs of TN from septic
Water Year 2014: 16,500 lbs of TN from septic
Water Year 2015: 13,000 lbs of TN from septic
Recent USGS SPARROW results estimate that 26% of the total nitrogen load leaving the watershed may be contributed by septic systems3:
Water Year 2013: 37,000 lbs of TN from septic
Water Year 2014: 92,000 lbs of TN from septic
Water Year 2015: 62,000 lbs of TN from septic
3Ator S.W. and Sekellick A.J. To be released as a 2016 USGS Open File Report
This information is preliminary and is subject to revision. It is being provided to meet the need for timely best science. The information is provided on the condition that neither the U.S. Geological Survey nor the U.S. Government shall be held liable for any damages resulting from the authorized or unauthorized use of the information.

## Slide 17
Metro Washington COG:
Landuse
Percent Impervious
0
25
50
75
100
Percent
Impervious1
Difficult Run
Watershed
Frederick County
Montgomery County
Loudoun
County
D.C.
Prince
George
County
Charles County
Fairfax
County
Prince
William
County
Frederick County
Montgomery County
Loudoun
County
D.C.
Prince
George
County
Charles County
Fairfax
County
Prince
William
County
Forested
Pasture/Hay
Row Crop
Low/High Development
Wetlands/Open Water
Landuse1
1Landuse and percent impervious from 2011 National Land Cover Dataset. http://www.mrlc.gov/nlcd2011.php

## Slide 18
Metro Washington COG:
Septic System Density
Frederick County
Montgomery County
Loudoun
County
D.C.
Prince
George
County
Charles County
Fairfax
County
Prince
William
County
Septic System Density
Low
High
Difficult Run
Watershed
Septic system density =
(total population in 2010) * (% of population on septic in 19901)
This information is preliminary and is subject to revision. It is being provided to meet the need for timely best science. The information is provided on the condition that neither the U.S. Geological Survey nor the U.S. Government shall be held liable for any damages resulting from the authorized or unauthorized use of the information.
11990 septic ratio = (person per household * housing units with septic) / total population. Values based on U.S. Census data.

## Slide 19
Nitrate concentrations from two watersheds with a high septic system density do not show seasonal variability or stormflow responses expected from inputs of N from fertilizer.
Evidence of Septic Leachate
Nitrate isotopes are suggestive of septic system effluent.
In general, nitrogen mass balances show septic system effluent to be a greater input than fertilizer leachate.
Empirical nitrate concentrations are significantly correlated with septic system density.
Although there tends to be a greater potential for fertilizer application in areas underlain by septic systems, septic system effluent appears to be the dominant source of nitrogen in Difficult Run and in similar Fairfax County watersheds.
Nitrogen concentrations and loads have increased at the Difficult Run downstream monitoring location1.
Septic Effluent vs Fertilizer Leachate
Jimmy Webber
jwebber@usgs.gov
Ken Hyer
kenhyer@usgs.gov
John Jastram
jdjastra@usgs.gov
JK Böhlke
jkbohlke@usgs.gov
Unresolved Questions….
How would changes to the septic infrastructure affect water-quality?
How quickly would water-quality respond to changes in landuse?
What are the transport processes and fate of HF-183 within the watershed?
1Based on long-term WRTDS trends in total nitrogen and nitrate flux and concentration. http://cbrim.er.usgs.gov/index.html
Preliminary Information-Subject to Revision. Not for Citation or Distribution
Judy Denver
jmdenver@usgs.gov
Michael Langland
Langland@usgs.gov
Water-Quality Monitoring in an
Urban Watershed:
The Influence of Septic Systems on
Nitrate Concentrations
and Spatial Patterns
December 12th, 2016

## Slide 20
Metro Washington COG:
SPARROW: Septic System Density
Hyer and others, 2016
Frederick County
Montgomery County
Loudoun
County
D.C.
Prince
George
County
Charles County
Fairfax
County
Prince
William
County
Septic System Density
Low
High
Difficult Run
Watershed