## Slide 1: VIRGINIA PHASE III DRAFT WIP
COG WRTC Meeting
May 7, 2017

## Slide 2: Schedule
Draft WIP Posted: April 5, 2019
Public Comment: April 12 – June 7, 2019
Final WIP Posted: August 9, 2019
DEQ web page:
https://www.deq.virginia.gov/Programs/Water/ChesapeakeBay/ChesapeakeBayTMDL/PhaseIIIWatershedImplementationPlanning.aspx

## Slide 3: Virginia Draft WIP III Document
DEQ Planning at Major Basin Scale
Potomac – Shenandoah Basin
  26 Counties/Cities
  6 Planning District Commissions
  12 Soil and Water Conservation Districts
Chart: 
| Agricuulture | Developed (MS4) | Developed (Non-MS4) | Natural
2017 | 22.8 | 5.6 | 13.1 | 58.5
2025 | 22.3 | 5.7 | 13.7 | 58.3
Chart: 
| Agricuulture | Developed (MS4) | Developed (Non-MS4) | Natural
2025 | 22.3 | 5.7 | 13.7 | 58.3
Column1
2017 versus 2025 Modeled Land Use for Virginia’s Potomac River Basin
Potomac River Basin | 2017 Progress | 2025 Basin Target | 2017 Gap to Target | 2017 Gap to Target + Climate Change
Nitrogen | 17,109,000 | 16,000,000 | 1,109,000 | 1,729,000
Phosphorus | 1,976,000 | 1,892,000 | 84,000 | 166,000
Natural
Agriculture
Non-MS4

## Slide 4: Wastewater Strategy
Commonwealth “Blurb”
  Achieve Additional Reductions from Significant Municipal WWTPs.
  Require reporting of sewer connections by wastewater utilities.
  VDH to establish by regulation TN limits for all OSS dispersing greater than 1,000 gallons per day (GPD), including Conventional OSS.
Potomac – Shenandoah River Basin
  38 Major Facilities (>1.0 MGD)
  85 Facilities (0.9 – 0.1 MGD
  67 Facilities (0.09 – 0.01 MGD)
  1085 Facilities (0.009 – 0.006 MGD)
“As of 2017, loads are well below the WLA limits, at 2.34 million pounds nitrogen and 140,600 pounds phosphorus for the Potomac Basin. The expectation through 2025 is that these loads will generally be maintained at those levels, but will slowly increase beyond 2025 as population increases continue in the Potomac River Basin.”

## Slide 5: Developed Lands Strategy
Commonwealth “Blurbs” –
Enhance Reporting of BMP Implementation
Fund VCAP; Fund SLAF; Define SLAF Needs
Establish Long-Term Partnership with PDCs
Expand Healthy Virginia Lawns Program
Pilot Urban NMP for Virginia Youth
Enhance the VDACS Certified Fertilizer Applicator Program
Promote Proper Use of Lawn Fertilizer
Enhance DOF Presence in Urban Centers with Focus on Canopy Goals, Riparian Plantings and Community Engagement
Establish 5-year program review of VSMP Authorities
Re-evaluate post-construction water quality requirements under the VSMP
Add nutrient management provisions to E&S requirements

## Slide 6: Municipal Separate Storm Sewer Systems (MS4s) Strategy
32 – MS4 Permitttees Potomac – Shenandoah River Basin
Implement Action Plans as required by permit or regulation
Virginia will honor its commitment to Permitttees allowing them three full permit cycles (5%, 35%, 60%) to meet their reductions requirements.
Any gap in this sector meeting its permit requirements by 2025 that are due to timing will be offset by the excess capacity achieved in the wastewater sector.
Observations –
  no mention of changes to required reduction amounts but does state “plan proposes to maintain the previously established MS4 requirements”
  WIP assumes 100% achievement N; 100 lb shortfall P

## Slide 7: Natural and Non-MS4 Developed
Agricultural, natural and non-MS4 developed lands were developed through the local and regional engagement (WIP III Initial).
The BMPs, “assuming sufficient resources are made available”, result in reductions of 1.37 million pounds of nitrogen and 214,800 pounds of phosphorus from 2017 levels.
Additional state policy initiatives will be needed to meet the Commonwealth’s reduction targets for 2025.
  461,000 lbs N; 60,200 lbs P
Nutrient exchanges (N:P) and Basin:Basin transfer from James to close gap
  104,000 lbs N - Potomac N:P
  585,000 lbs N – James N
  62,000 lbs P – Potomac N:P

## Slide 8: Natural and Non-MS4 Developed BMP Major Adjustments
BMP | WIP II | WIP IIII Draft | Units
Stream Restoration | 24,491 | 168,786 | Feet
Shoreline Management | 0 | 2,003,605 | Feet
Storm Drain Cleaning | 0 | 308,120 | lbs
Grey Infrastructure(IDDE) | 0 | 17,301 | Acres
Permeable Pavement | 30 | 4,314 | Acres
Storm Water Treatment Performance Standard | 0 | 19,982 | Acres
 |  |  | Acres
Tree Planting - Canopy | 0 | 19,463 | Acres
Forest Buffer | 1,420 | 13,043 | Acres
Forest Planting | 325 | 6,218 | Acres
Septic Pumping | 18,630 | 28,619 | Systems
Plan strongly shifts towards BMPs that many localities have limited experience when it comes to review, reporting, inspection, and verification.
(source: CAST)

## Slide 9: N Load Sources by Source Sector: Potomac (source: CAST)
Nitrogen Source Sector | 2017 Progress V9 | VA Specified WIP 2 | VA Draft WIP 3 April 10, 2019 | Change in Load WIP II/III (M lbs) | Change in Load WIP II/III (%)
Agriculture | 7,211,361 | 3,507,711 | 5,181,240 | 1.67 | 0.10
Developed | 3,623,359 | 3,353,382 | 3,237,298 | -0.12 | -0.01
Natural | 3,109,845 | 3,036,258 | 2,999,500 | -0.04 | -0.01
Septic | 822,474 | 813,537 | 818,899 | 0.01 | 0.00
Wastewater | 2,341,680 | 4,375,371 | 3,344,117 | -1.03 | -0.08
Total (M lbs) | 17.11 | 15.09 | 15.58 | 0.49 | 
( - ) Change in % Load represents more stringent condition

## Slide 10: P Load Sources by Source Sector: Potomac (source: CAST)
Phosphorus Source Sector | 2017 Progress V9 | VA Specified WIP 2 | VA Draft WIP 3 April 10, 2019 | Change in Load WIP II/III (M lbs) | Change in Load WIP II/III (%)
Agriculture | 796,476 | 371,900 | 525,304 | 0.15 | 0.09
Developed | 504,099 | 472,455 | 443,827 | -0.03 | -0.02
Natural | 534,624 | 513,847 | 477,649 | -0.04 | -0.03
Septic | 378 | 378 | 378 | 0.00 | 0.00
Wastewater | 140,622 | 298,372 | 240,911 | -0.06 | -0.04
Total (M lbs) | 1.98 | 1.66 | 1.69 | 0.03 | 
( - ) Change in % Load represents more stringent condition

## Slide 11: Some General WIP Conclusions
The WIP calls for N and P reductions from the developed land sector which greatly exceed the historical pace of BMP implementation reported by in the last ten years; especially for nonregulated developed land.
Detailed levels of additional state funding for urban BMP implementation are not offered in the WIP. State funding is always conditional on approval by the state legislature, which has not always fully supported prior budget requests.
The WIP depends on a significant expansion of urban nutrient management planning across public and private lands in the Commonwealth.
The WIP strongly shifts towards BMPs that many localities, especially nonregulated localities, have limited experience when it comes to review, reporting, inspection, and verification.
Questionable as to whether the state/local forestry agencies have the resources to meet the extremely higher demand for new forestry practices/implementation in the next decade envisioned by the WIP.