## Slide 1: COG’s Round 8.2 Cooperative Forecast & Regional Wastewater Flow Projections
COG staff - Presentation to WRTC
September 6, 2013

## Slide 2: Overview
COG’s Wastewater Treatment Plants
  Focus on Major Plants (defined as => 2 mgd)
    20 – Including both Dale Service Corp plants
  Service Area (SA) maps – being confirmed/updated
    SAs shown for Majors, though ‘Other’ still being refined
COG’s Regional Cooperative Forecast Process
  Round 8.2 – recently adopted by COG Board
COG’s Regional Wastewater Flow Forecast Model (RWFFM)
  Basic assumptions
  Demographic trends for Majors
  Flow projections – Unadjusted & Adjusted
    Remaining regional capacity

## Slide 4: COG’s Regional Cooperative Forecast Process
Round 8.2 Cooperative Forecast adopted by COG Board on July 10, 2013
Demographic projections are based on Jurisdictions’ forecasts and are within 3 percent of the econometric model projections
  Population, employment, and households
Demographic information is allocated from Transportation Analysis Zones (TAZs) to the appropriate wastewater service areas (i.e., sewersheds and sub-sewersheds)

## Slide 5: COG’s RWFFM – Basic Assumptions
Regional model grown from original Blue Plains work
Wastewater projections derived employment & households and Flow Factors (not population)
Black & Veatch updated Base Year Flows (BYF) & flow factors for Blue Plains in 2010
  2009 BYFs are actual annual average flows
  I/I rate of 44% of incremental sanitary flow remained the same
Used Ffx #’s for VA plants & WSSC #’s for MD plants
Table ES-2 – 2009 Approved Flow Factors |  |  |  |  |  | 
Category | Fairfax County | WSSC | Loudoun Water | District | Dulles VA | Vienna VA
Household (gpd/unit) | 150 | 180 | 185 | 170 | NA | 170
Employment (gpd/employee) | 30 | 28 | 25 | 25 | 48 | 21-50

## Slide 6
Chart: Demographic Projections for COG Region Served by Major WWTPs (=> 2 mgd) Round 8.2
| 2009 | 2010 | 2015 | 2020 | 2025 | 2030 | 2035 | 2040
Household | 1665660 | 1680277 | 1789207 | 1887990 | 1987925 | 2074509 | 2152257 | 2225600
Employment (includes industrial, office, retail, & others) | 2808141 | 2826122 | 2998947 | 3250095 | 3471395 | 3675509 | 3848274 | 4034736
Population | 4408515 | 4458692 | 4718368 | 4942343 | 5177083 | 5376621 | 5552299 | 5718086
COG Total
5 million

## Slide 7: COG Major WWTPs & ‘Unadjusted’ Flow Projections (Draft)
Unadjusted flows reflect only impact of demographic trends

## Slide 8: COG Major WWTPs & ‘Unadjusted’ Flow Projections (Draft)
Unadjusted flows reflect only impact of demographic trends
Total Regional Capacity (for Majors) – 776 mgd

## Slide 9: COG Major WWTPs & ‘Adjusted’ Flow Projections (Draft)
Adjusted flows reflect impact of (significant) flow reductions & flow diversions
Total Regional Capacity (for Majors) – 776 mgd
718 mgd = 93% of Total Capacity

## Slide 10
COG’s Region Forward and Economy Forward initiatives

## Slide 11: Next Steps
Continue to verify with WWTP operators:
  WWTP service area maps
  Flow projections/assumptions
  Refine maps re: septic/distributed systems vs. non-sewered areas
Present overall/regional findings to CBPC (9/20/13)
Region Forward
  Report on ‘percent wastewater capacity’ findings
  Overall RAC’s on WWTP Service Areas
Flow vs. Load Capacity Analysis
  Outgrowth of work being done for Blue Plains Users

## Slide 12: Wrap-up
Questions?
Ideas?
Additional presentations:
  COG’s Cooperative Forecast process
  COG’s RWFFM
  CBP’s use to characterize/project growth
Many thanks for teamed effort – Mukhtar Ibrahim, Nasser Ameen, & Lana Sindler
Contact: Tanya Spano (202) 962-3776 / tspano@mwcog.org