## Slide 1: COG’s Multi-Sector Working Group Energy/Built Environment Subgroup
Metropolitan Washington Council of Governments
March 19, 2015
Greenhouse Gas - Multi-sector Working Group

## Slide 2
NCR Greenhouse Gas Inventory
2005 Revised GHG Inventory
National Capital Region
MWCOG
74.02 MMtCO2e
16.02 MtCO2e/capita
2012 Preliminary GHG Inventory
National Capital Region
MWCOG
69.88 MMtCO2e
13.30 MtCO2e/capita
Chart: 
 | 0.33056 | 0.038555 | 0.38845 | 0.17859 | 0.0060359 | 0.021413 | 0.0364
Chart: 
 | 0.29911 | 0.05431 | 0.40476 | 0.19859 | 0.0037828 | 0.0045934 | 0.034855
Note: Due to differences in methodologies, 2005 and 2012 inventories are not directly comparable.

## Slide 3
NCR Greenhouse Gas Inventory
National Capital Region Greenhouse Gas Inventory - MWCOG |  |  |  | 
 | 2005 Revised |  | 2012 Preliminary | 
Source | MMT CO2e | Percent of Total | MMT CO2e | Percent of Total
On Road Transportation | 22.14 | 30% | 23.10 | 33%
Commercial Airline | 4.02 | 5% | 2.69 | 4%
Electricity | 29.96 | 40% | 27.15 | 39%
RCI Fuel | 14.70 | 20% | 12.48 | 18%
Solid Waste | 0.28 | 0.4% | 0.42 | 0.6%
Wastewater Treatment | 0.34 | 0.5% | 1.50 | 2%
Hydrofluorocarbons (HFC) | 2.58 | 3% | 2.54 | 4%
Total (Gross Emissions) | 74.02 | 100% | 69.88 | 100%
Per Capita GHG Emissions | 16.02 |  | 13.30 | 

## Slide 4
NCR Greenhouse Gas Inventory
2005 & 2012 Greenhouse Gas Inventory Methodologies
Source | 2005 General Methodology | 2012 General Methodology
On Road Transportation | Moves 2010a; 2014 CLRP; TPB Travel Demand Model v 2.3.57 | Moves 2010a; 2014 CLRP; TPB Travel Demand Model v 2.3.57
Commercial Aviation | Total US commercial aviation from EPA US GHG Inventory scaled to region based on Bureau of Transportation Statistics miles for all arriving and departing flights divided by two | Total US commercial aviation from EPA US GHG Inventory scaled to region based on Bureau of Transportation Statistics passenger miles for all arriving passengers scaled to the region by % trips originating in the region
Electrical | Emissions from regional power plants (EPA) plus emissions from electric imports (EPA regional emission factor) | Total electrical consumption times emission factors for eGrid zones covering Maryland/DC and Virginia

## Slide 5
NCR Greenhouse Gas Inventory
2005 & 2012 Greenhouse Gas Inventory Methodologies
Source | 2005 General Methodology | 2012 General Methodology
RCI Fuel | Total natural gas, distillate and residual fuel oil from US DOE, EIA, scaled to the region by population plus non-road emissions from EPA calculation tool | Total natural gas, distillate and residual fuel oil from US DOE, EIA, scaled to the region by households for residential and population for commercial and industrial plus non-road emissions from EPA tool
Solid Waste | US EPA waste GHG emission calculator | US EPA waste GHG emission calculator
Wastewater | EPA State Inventory Tool, IPCC formulas, default inputs, by population | ICLEI Wastewater emissions estimation tool based on treatment technology and population
HFC | Total US HFC emissions from EPA US GHG Inventory scaled to region by employment | Total US HFC emissions from EPA US GHG Inventory scaled to region by population