## Slide 1: NCHRP 03-133: Non-Motorized Users at Traffic Signals
Burak Cesme, PhD
Joint SPOTS & Traffic Signals Subcommittee Meeting
Washington, D.C.
December 5, 2019

## Slide 2: NCHRP 03-133: Traffic Signal Design and Operations Strategies for Non-Motorized Users
Develop toolbox of strategies and treatments to make traffic signals work better for peds/bikes
April 2018 – March 2020

## Slide 3: 3 “Raises/Razes”
Raise the roof
  Research and innovation – advance practice
Raise the floor
  Improve practice – adjust the status quo
Raze the barriers
  Improve processes for implementation

## Slide 4: SET 1: Basic Treatments to Reduce Pedestrian Delay
Evaluating Pedestrian and Bicycle Crossing Delay
Short Cycle Length
Maximizing Walk Interval Length
  General (Pre-timed Phases)
  Rest in WALK
  Adapting Minimum Green to Demand
  Adaptive Walk Intervals
  Changing from actuated to pre-timed
Recall versus Actuation for Pedestrians

## Slide 5
“Only what’s measured counts”
Policy: Whenever vehicular delay is reported, ped delay must be reported, too.
Basic Treatments to Reduce Pedestrian Delay
“Evaluating Pedestrian and Bicycle Crossing Delay”
Boston Example
Timing Plan 1: 123 s average ped delay
Timing Plan 2: 45 s average ped delay (with 0.5 s increase in vehicular delay)

## Slide 6
Less Pedestrian Delay, Less Transit Delay
Better Ped/Bike Compliance
Fewer Speeding Opportunities
Basic Treatments to Reduce Pedestrian Delay
“Short Cycle Length”
Amsterdam Policy:
Make cycles as short as possible
Maximum Cycle = 100 s

## Slide 7: “Maximizing WALK Interval Length”
Basic Treatments to Reduce Pedestrian Delay
but this:
[Make the WALK interval as long as will fit within the parallel vehicular phase]
Not this:
For coordinated phases, use the setting “Rest in WALK”

## Slide 8: SET 2: Eliminating Conflicts with Parallel Traffic Turns
Exclusive Pedestrian Phases
Protected Left Turns on Multilane Roads
Concurrent-Protected Pedestrian Crossings
Delta Islands (Channelized Right Turns) for Ped and Bike Crossings

## Slide 9
Eliminating Conflicts with Parallel Traffic Turns
“Protected Left Turns on Multilane Roads”
1
2
3
US Guidelines: Permitted lefts are OK unless:
50+ mph speed limit
Crossing 4+ lanes
Crash experience
  Contrary to Vision Zero principles
Amsterdam Policy: On multilane roads, left turns are protected only, never “permitted”.

## Slide 10
Eliminating Conflicts with Parallel Traffic Turns
“Concurrent-Protected Pedestrian Crossings”
a.k.a. Protected Right Turns, Right-Turn Overlap
Using right turn AND left turn signals to protect crossings from all turn conflicts

## Slide 11: SET 3: Mitigating Conflicts with Parallel Traffic Turns
Leading Pedestrian Intervals
Delayed Turn
Flashing Ped/Bike Crossing Warning

## Slide 12
“Leading Pedestrian Intervals”
a.k.a. Pedestrian Head Start
Mitigating Conflicts with Parallel Traffic Turns
Audible signal needed
May bikes use it, too?
Can make cycle longer – and so in Netherlands:
  NOT used where “protected intersection” layout gives peds/bikes a head start in space.
  Only used where bike & car have the same stopline
Leading interval (3-7 s): Peds only
Concurrent traffic with turn conflicts
Relative Stopline Setback

## Slide 13
“Delayed Turn”
a.k.a. Leading Bike Interval, Leading Thru Interval, LPI+
Mitigating Conflicts with Parallel Traffic Turns
Leading interval (10 s or more)
Charlotte (“LPI-Plus”)
New York, Charlotte: Only with a right turn lane
Montreal: Without a right turn lane

## Slide 14
“Flashing Ped/Bike Crossing Warning”
Mitigating Conflicts with Parallel Traffic Turns
Flashing Bike Crossing Warning, Amsterdam
Flashing Yellow Arrow
“LET OP” = WATCH OUT

## Slide 15: SET 4: Improving Ped/Bike Information and Ease
Pedestrian Countdown
Red Period Countdown
No Turn on Red
Independently Mounted Pushbuttons
Accessible Signals without Pushbuttons
Call Indicators
Serving Slower Pedestrians

## Slide 16: SET 5: Bicycle Phases and Special Bike Needs
Indicating Bike Phases
Detection for Bicycles
Minimum Green and Change Interval Settings for Bikes with Shared Traffic Signals

## Slide 17
“Indicating Bike Phases”
Bicycle Phases and Special Bike Needs
FHWA won’t allow bike green if there are permitted turn conflicts
Vehicles
Bikes
Peds

## Slide 18: SET 6: Special Phasing Techniques Favoring Peds and Bikes
Multi-Stage Crossings
  Progression through ped crossings
  Pedestrian Overlaps with Left Turn Phases and Different Lead-Lag Phasing Sequences
Pedestrian Phase Overlaps with Each Other, with Bike Phases, and with Vehicular Holds
Re-service for the Ped/Bike Phase
Two-Stage Left Turn Progression for Bikes
HAWK Signals at Intersections with Minor Streets

## Slide 19
“Re-service for the Ped/Bike Phase”
Special Phasing Techniques Favoring Peds and Bikes
Reservice: twice per cycle
Run free: on demand, allowing cars 10 s green between ped phases

## Slide 20: Questions?
Burak Cesme, PhD
bcesme@kittelson.com