## Slide 1
Ozone Season Summary
2014
Sunil Kumar
MWAQC-TAC Meeting, COG
September 9, 2014
Item #2

## Slide 2
Ozone Season Summary
[As of September 3, 2014]
Peak 8-Hour Ozone Concentrations (ppb)
Data based on the 8-hour standard set at 75 ppb. Since April 1, 2014, there have been:
4 Code Orange Days, 39 Code Yellow Days, 112 Code Green Days

## Slide 3: Meteorology Factors on Exceedance Days
August 6, 2014
  High Temperature: 90°F
  Light winds
  Northwesterly winds brought NOx and ozone from the Ohio River Valley
  Clear Skies due to a high pressure system
  Similar conditions during the two days prior caused ozone to build up
August 27, 2014
  High Temperature: 90°F
  Northwesterly winds brought NOx and ozone from Western PA and OH
  High ozone values in Western PA on August 26
  Clear and sunny skies

## Slide 4: Wind Trajectories for 8/6 and 8/27

## Slide 5: Ozone Concentration at 3 PM
August 26
Ozone concentrations = 70-80 ppb
24 – 32 hours

## Slide 6: Ozone Concentration at 3 PM
August 27
Ozone concentrations = 70-90 ppb

## Slide 7
2014 Ozone Exceedances
Analysis is based on draft data until September 3, 2014. Data is subject to change.
Date | Monitors Exceeding | Highest Monitor | 8-Hr Max (ppb)
6/16/2014 | 4 | Arlington | 87
7/11/2014 | 1 | Prince William | 76
8/6/2014 | 1 | Charles County | 77
8/27/2014 | 2 | Arlington/Prince George County (tie) | 76

## Slide 8
Ozone Exceedance Trend
2014 analysis is based on draft data as of September 4, 2014 and is subject to change.
Chart: Number of Exceedance Days - 2008 Ozone Standard (75 ppb) Breakdown of Code Orange, Red, and Purple Days 1997 - 2014
| 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014
orange | 38 | 46 | 47 | 24 | 34 | 40 | 19 | 19 | 38 | 28 | 40 | 17 | 4 | 30 | 18 | 18 | 4 | 4
red | 12 | 20 | 16 | 3 | 9 | 14 | 2 | 3 | 4 | 5 | 3 | 3 | 0 | 3 | 2 | 3 | 0 | 0
purple | 3 | 1 | 2 | 1 | 0 | 4 | 2 | 1 | 0 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
total | 53 | 67 | 65 | 28 | 43 | 58 | 23 | 23 | 42 | 35 | 43 | 20 | 4 | 33 | 20 | 21 | 4 | 4

## Slide 9
90 Degree Days and Exceedance Days
2014 analysis is based on draft data as of September 3, 2014 and is subject to change.
Chart: 90 Degree Days (Dulles) and 2008 Ozone NAAQS Exceedance Days
| 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014
Exceedance Days | 53 | 67 | 65 | 28 | 43 | 58 | 23 | 23 | 42 | 35 | 43 | 20 | 4 | 33 | 20 | 21 | 4 | 4
90F Days | 32 | 37 | 39 | 11 | 18 | 41 | 14 | 7 | 33 | 37 | 53 | 29 | 21 | 58 | 42 | 40 | 18 | 13

## Slide 10
Why Fewer Exceedance Days Now ?
Emission Control Programs
Federal | State | Local
Acid Rain Program (1996/2000) | Vehicle Inspection and Maintenance Programs | Renewable Energy Programs Regional Wind Power Purchase Program Clean Energy Rewards Program Renewable Portfolio Standards
Tier 2 (LD Vehicle) Rule (2004) | MD Healthy Air Act (2009/2012) | Energy Efficiency Programs LED Traffic Signal Retrofit Program Building Energy Efficiency Programs
HD Diesel Vehicle Rule (2004/2007) | VA CAIR Rule | VRE Idling Reduction
NOx SIP Call (2004) | DC CAIR Rule | Low VOC Paint
Clean Air Interstate Rule (2009) | Ozone Transport Commission Rules | Gas Can Replacement

## Slide 11
Ozone Design Value Trend
Chart: 8-hour Ozone Design Value Washington, DC-MD-VA Ozone Nonattainment Area (1999-2014)
| 1997-99 | 1998-00 | 1999-01 | 2000-02 | 2001-03 | 2002-04 | 2003-05 | 2004-06 | 2005-07 | 2006-08 | 2007-09 | 2008-10 | 2009-11 | 2010-12 | 2011-13 | 2012-14*
HIGHEST | 106 | 101 | 97 | 97 | 99 | 96 | 91 | 91 | 91 | 87 | 80 | 81 | 82 | 87 | 81 | 76
NAAQS | 75 | 75 | 75 | 75 | 75 | 75 | 75 | 75 | 75 | 75 | 75 | 75 | 75 | 75 | 75 | 75
1997 NAAQS | 84 | 84 | 84 | 84 | 84 | 84 | 84 | 84 | 84 | 84 | 84 | 84 | 84 | 84 | 84 | 84

## Slide 12
4th Highest Ozone Value
Chart: 4th Highest 8-hour Ozone Maximum Concentration Washington, DC-MD-VA Ozone Non-Attainment Area 1999-2014
| 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014*
2008 NAAQS | 0.075 | 0.075 | 0.075 | 0.075 | 0.075 | 0.075 | 0.075 | 0.075 | 0.075 | 0.075 | 0.075 | 0.075 | 0.075 | 0.075 | 0.075 | 0.075
1997 NAAQS | 0.084 | 0.084 | 0.084 | 0.084 | 0.084 | 0.084 | 0.084 | 0.084 | 0.084 | 0.084 | 0.084 | 0.084 | 0.084 | 0.084 | 0.084 | 0.084
4th Highest 8-Hour Max Ozone | 0.106 | 0.094 | 0.101 | 0.112 | 0.097 | 0.093 | 0.092 | 0.095 | 0.089 | 0.085 | 0.071 | 0.089 | 0.087 | 0.09 | 0.072 | 0.071

## Slide 13
These 4th highest 8-hour ozone values in 2015 would lead to non-attainment in 2015
Analysis is based on draft data until September 3, 2014. Data is subject to change.
Site | 4th Highest 8-Hour Max Ozone Concentration (ppm)
Beltsville | 0.087
PG Equestrian | 0.090
Arlington | 0.090
Calvert | 0.091
Franconia | 0.092
Southern Maryland | 0.094
Rockville | 0.095
HU- Beltsville | 0.095
McMillian NCore | 0.096
Frederick | 0.096
Ashburn | 0.099
Long Park | 0.100

## Slide 14
Fine Particle Summary
[As of September 3, 2014]
24-hour PM2.5 Average (µg/m3)
Data based on the 24-hour standard set at 35 µg/m3. Since April 1, 2014, there have been:
49 Code Yellow Days, 106 Code Green Days

## Slide 15
PM2.5 Exceedance Trend
Chart: Number of Exceedance Days - 2006 24-Hour PM2.5 Standard (35 µg/m3) Breakdown of Code Orange, Red, and Purple Days (Washington, DC Region : 1999 - 2014)
| 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014
orange | 13 | 16 | 25 | 14 | 11 | 11 | 14 | 7 | 6 | 4 | 1 | 7 | 0 | 3 | 0 | 0
red | 2 | 0 | 0 | 3 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0
purple | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Total Exceed. | 15 | 16 | 25 | 17 | 12 | 11 | 14 | 8 | 6 | 4 | 1 | 8 | 0 | 3 | 0

## Slide 16
24-Hour PM2.5 Design Value Trend
Chart: 24-Hour PM2.5 Design Value Washington D.C. Region: 2003-2013
| 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013
 | 44 | 42 | 38 | 37 | 35 | 32 | 29 | 27 | 26 | 27 | 25
 | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 35

## Slide 17
Annual PM2.5 Design Value Trend
Chart: Figure 16: PM2.5 Annual Design Values Washington, D.C. Region, 2003-2013
| 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013
 | 15.8 | 15.1 | 14.8 | 14.5 | 14.2 | 13.1 | 12.1 | 11.3 | 10.7 | 10.5 | 10.1
 | 15 | 15 | 15 | 15 | 15 | 15 | 15 | 15 | 15 | 15 | 15
NAAQS PM2.5 (2012) | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12